## Slide 1: Exhaust Emissions from In-Use General Aviation Aircraft
ACRP 02-54
Tara I. Yacovitch,* Zhenhong Yu, Scott C. Herndon, Rick Miake-Lye
Aerodyne Research, Inc. Billerica, MA
*tyacovitch@aerodyne.com (978) 932-0228
David Liscinsky
United Technologies Research Center, East Hartford, CT
W. Berk Knighton
Department of Chemistry & Biochemistry, Montana State University, Bozeman, MT
Mike Kenney, Cristina Schoonard, Paola Pringle
KB Environmental, St Petersburg, FL
April 2016

## Slide 2: Air Quality at Airports

## Slide 3: ACRP 02-54: Measuring and Understanding Emission Factors for General Aviation Aircraft
Verify existing data
Supplement existing data
Recommend substitutions
Only 8 piston engines!
Continental Motors, Inc. | 6-285-B
Curtiss-Wright | R-1820
Lycoming Engines | IO-320-D1AD
Lycoming Engines | IO-360-B
Lycoming Engines | O-200
Lycoming Engines | O-320
Lycoming Engines | TIO-540-J2B2
Lycoming Engines | TSIO-360C

## Slide 4: Approach
Data Collection
Flight schools, private pilots (volunteers or fuel vouchers)
Direct measurements : engines in airframe
Simulate all power states on the ground
Analysis
Impact of new emission factors on airports
Recommendations

## Slide 5: Emissions Compounds
Nitrogen oxides
NOx = NO + NO2
Carbon Monoxide
CO
Total Hydrocarbons
HC = methane +
ethane +
… +
benzene +
…
Particulate Matter
PM
PM
number
volatile
non-volatile
mass
volatile
non-volatile
Carbon Dioxide
CO2

## Slide 6: Emissions Indices
Most sensitive fast gas instruments in the world.
“plume” =
Excess CO2, CO, HC, NOx, …
Fuel CO2
(g CO2/ kg Fuel):
3067 for AVGAS 100LL
3160 for Jet A

## Slide 7: Power States
Idle
Cruise
Approach
International Civil Aviation Organization
Landing Take-off Cycle

## Slide 8: Results
How many engines were measured?
What are the main conclusions?

## Slide 9: Measured Aircraft
60 Engine Tests
47 Full Engine Tests (all power states)
26 Unique Full Engine Tests
2 gas turbines
45 pistons: 16 Lycoming O-320, 6 Lycoming O-360, 4 Continental O-200, 4 Lycoming IO-360, 4 Lycoming IO-540, and more…

## Slide 10: Piston Engines are Drastically Different From Gas Turbine Engines
Piston
Gas Turbine
CO
NOx

## Slide 11: Piston Engines are Drastically Different From Gas Turbine Engines
Piston
Gas Turbine
CO
NOx
HC
nvPMm

## Slide 12: Piston Engines are Drastically Different From Gas Turbine Engines
Piston
Gas Turbine

## Slide 13: Overall Trends
CO
NOx
HC
nvPMm
GA Piston Engines | GA Gas Turbines
CO very high | CO is very low
NOx is low (usually) | NOx is higher (usually)
HC is high and mostly unburned fuel | HC is low and partially combusted
volatile PM dominate | volatile PM dominate
PM size is <20nm | PM size is 10 – 70 nm
Fuel flow is very low | Fuel flow is relatively high
High inherent variability | Low inherent variability

## Slide 14: Piston Engines are more Variable Than Gas Turbine Engines
Piston
Gas Turbine

## Slide 15: Why So Variable?
Low Combustion Efficiency
Simple Analog Controls
Limited Diagnostics
Rugged Old Technology
Pilot mindset
Throttle
Mixture
Propeller RPM
Exhaust Gas Temp (non-standard!)
Each piston’s temperature behaves differently
http://www.swaircraftappraisals.com/MeyersForum/Engine%20Info/Engine%20Operation/Pelican's%20Perch%20Mixture%20Magic.htm

## Slide 16: Distributions of Piston Engine Emissions Show Trends with Power State
linear axes

## Slide 17: Distributions of Piston Engine Emissions Show Trends with Power State
note logarithmic axis! (except for CO)
HC decreases with power
NOx peaks at cruise power
the leaner the fuel/air mixutre, the higher the NOx

## Slide 18: Airport Emissions Calculations
How do the results from ACRP 02-54 impact the modeled emissions from a hypothetical airport?

## Slide 19: Sensitivity Analysis
Hypothetical Airport:
  fleet characteristics based on national registry
  40 aircraft
  ~ 97K airport operations per year
  37 pistons (99% of ops)
  3 gas turbines (1% of ops)
Simulation choices:
  default time-in-mode
  substitutions based on engine HP, airframe, etc.

## Slide 20: Effect of Variability on Airports
Baseline Scenario
Average Measured EIs
Updated Scenarios
AEDT EIs only
Confidence Limits from variability
Standard method
  FAA-mandated software
  use averages and upper limits
Monte-Carlo method
  random sampling from source data
  run simulation for large numbers to get confidence limits

## Slide 21: Comparing Variable Data
The variability of an average emission can be measured using 95% confidence intervals.
A confidence interval = upper limit & lower limit
We are 95% sure that the true average emission falls between these limits.
Existing data is considered invalid (statistically different) if it falls outside this confidence intervals.
statistically different
statistically “the same”
upper
limit
lower
limit
average
confidence interval

## Slide 22: Standard Method Simulation Results: AEDT/EDMS
CO emissions similar
HC and NOx emissions larger
Baseline ~ Updated
  baseline scenario falls within 95% confidence intervals of updated scenario
  data is too variable!
Assumes normal statistics
  true for CO
  false for other species!
https://en.wikipedia.org/wiki/Log-normal_distribution

## Slide 23: Alternate Method: Monte-Carlo
Use a sample to simulate a population
Confidence intervals based on real measured distributions (no assumptions on their shape)
Hypothetical Airport
engine types, operations
Sample Data Pool
EI, fuel flow, times in mode
random draw
from engine matches
Weekly Airport Emissions
Emissions Burden per LTO
EI x fuel flow x times

## Slide 24: Alternate Method: Monte-Carlo
Despite variability, yearly inventory can be pinned down
Good, plentiful data is crucial
Assumptions should be verified
  GA times-in-mode
  High HP engines
  Fleet use (flight schools vs individual-owned)

## Slide 25: Impact on Airports
GA airport emissions are higher than previously thought for HC and NOx, similar for CO.
Variability in piston engine emissions leads to enormous uncertainties using standard procedures.
Monte-Carlo methods have the potential to reduce these uncertainties, but require large datasets of emissions that are representative of real operations.

## Slide 26: Policy Implications
“lean it out”
Variability and skewed distributions
  average emission is not the most common emission!
Research impact of lean(er) idle and taxi
  HC with risk of NOx
Pinning down airport emissions is possible
  large sample sizes of representative data
  Monte-Carlo methods
“full rich at all times”
https://en.wikipedia.org/wiki/Log-normal_distribution

## Slide 27: Future Research Opportunities
Representative fleet, operations and times-in-mode
Fuel additives
Large dataset collection of emission indices
Partitioning of emissions (eg. HC to VOCs)

## Slide 28: Acknowledgements
  Marci Greenberger
ACRP 02-54 Panel
  Karen Scott
  Patti Clark
  Robert Freeman
  Sam Hartsfield
  Corbett Smith
  Phillip Soucacos
Airport managers and host airports, including:
  Stephen Bourque and the users at Boire Field
  Robert Mezzetti and the Beverly Regional Airport
Pilots, flight schools, fixed base operators, charter services and companies, including:
  Joe Sarcione
  Mark Scott at Falcon Air
  Arne Nordeide at Beverly Flight Center
  Paul Beaulieu at Perception Prime Flight Instruction
  Ron Emond at Air Direct Airways
  Drew Gillett
  Sheera Kaizerman
  Brian Stoughton
  Aeroptic, LLC.

## Slide 29: Questions?