NCHRP Project 17-45:

Enhanced Safety Prediction Methodology

And Analysis Tool for Freeways and Interchanges

Freeway and Interchange Safety Evaluation Workshop

Course Notes

July  2013

Freeway and Interchange Safety Evaluation Workshop

Workshop developed as part of NCHRP Project 17-45:

Enhanced Safety Prediction Methodology and Analysis Tool for Freeways and Interchanges

Date:

Location:

Instructor:

Agenda

9:00	Introduction

9:30	Lesson 1: Overview of Safety Evaluation

10:30	Break

10:45	Lesson 2: Overview of Software Tool

12:00	Lunch Break

1:00	Lesson 3: Freeway Segments

2:35	Break

2:50	Lesson 4: Interchange Ramps

3:35	Lesson 5: Crossroad Ramp Terminals

4:25	Lesson 6: Applications

4:45	Wrap-up and Adjourn

Course Materials:	Course Notes

Enhanced Interchange Safety Analysis Tool software (on CD)

ISATe User Manual

WORKSHOP EXERCISES

1:  Freeway Segment

2:  Freeway Segment

3:  Freeway Segment

4:  Freeway Segment

5:  Freeway Section

6:  Ramp Segment

7:  Ramp Segment

8:  Entire Ramp

9:  Ramp Terminal

10:  Ramp Terminal

11:  Interchange Terminals

EXERCISE 1:  FREEWAY SEGMENT

Location:  Segment 1 on urban six-lane freeway section

Study period:  2013 to 2015				Area type: urban

Crash data description: No crash data

INPUT DATA

Basic Roadway Data

Number of lanes: 6

Segment length:  0.30 mi

Alignment Data

Horizontal curve in segment:  No

Cross Section Data

Lane width:  11 ft

Outside shoulder with:  6 ft

Inside shoulder width:  4 ft

Median width:  50 ft

Rumble strips on outside shoulders:  Yes, full length of segment

Rumble strips on inside shoulders:  Yes, full length of segment

Presence of barrier in median:  None

Roadside Data

Clear zone width:  15 ft

Presence of barrier on roadside:  None

Ramp Access Data

Travel in Increasing Milepost Direction

Ramp entrance in segment:  No

Distance from begin milepost to upstream entrance ramp gore:  0.7 mi

Ramp exit in segment:  No

Distance from end milepost to downstream exit ramp gore:  0.5 mi

Type B weave in segment:  No

Travel in Decreasing Milepost Direction

Ramp entrance in segment:  No

Distance from end milepost to upstream entrance ramp gore:  0.5 mi

Ramp exit in segment:  No

Distance from begin milepost to downstream exit ramp gore:  0.7 mi

Type B weave in segment:  No

EXERCISE 1:  FREEWAY SEGMENT (continued)

Traffic Data

Proportion of AADT during high-volume hours:  Use default

Freeway Segment Data

AADT (year 2014):  86,000 veh/d

Ramp Data

AADT (year 2014):  6,100 veh/d (all ramps)

Crash Data

Not available

OUTPUT SUMMARY

What is the total predicted number of crashes?  ……………………………...

EXERCISE 1a:  FREEWAY SEGMENT

Location:  Segment 1 on urban six-lane freeway section

Study period:  2013 to 2015				Area type: urban

Crash data description: Data for each individual segment

Crash period:  2005 to 2007

INPUT DATA

Traffic Data

Freeway Segment Data

AADT (year 2006):  82,000 veh/d

AADT (year 2014):  86,000 veh/d

Ramp Data

AADT (year 2006):  6,000 veh/d (all ramps)

AADT (year 2014):  6,100 veh/d (all ramps)

Crash Data

| Crash Type | Count |
| --- | --- |
|  | Fatal-and-injury | Property-damage-only |
| Multiple-vehicle | 3 | 4 |
| Single-vehicle | 1 | 1 |
| Ramp-entrance-related | 0 |
| Ramp-exit-related | 0 |
| Note: Counts can be entered for any years in the crash period (crash year is not used in ISAT). |

OUTPUT SUMMARY

What is the total expected number of crashes?  …………………….............

EXERCISE 2:  FREEWAY SEGMENT

Location:  Segment 2 on urban six-lane freeway section

Study period:  2013 to 2015				Area type: urban

Crash data description: Data for each individual segment

Crash period:  2005 to 2007

INPUT DATA

Basic Roadway Data

Number of lanes: 6

Segment length:  0.10 mi

Alignment Data

Horizontal curve in segment:  No

Cross Section Data

Lane width:  11 ft

Outside shoulder with:  6 ft

Inside shoulder width:  4 ft

Median width:  50 ft

Rumble strips on outside shoulders:  Yes, full length of segment

Rumble strips on inside shoulders:  Yes, full length of segment

Presence of barrier in median:  None

Roadside Data

Clear zone width:  15 ft

Presence of barrier on roadside:  None

Ramp Access Data

Travel in Increasing Milepost Direction

Ramp entrance in segment:  Lane add

Ramp exit in segment:  No

Distance from end milepost to downstream exit ramp gore:  0.4 mi

Type B weave in segment:  Yes

Length of weaving section:  0.5 mi

Length in segment:  0.1 mi

Travel in Decreasing Milepost Direction

Ramp entrance in segment:  No

Distance from end milepost to upstream entrance ramp gore:  0.4 mi

Ramp exit in segment:  No

Distance from begin milepost to downstream exit ramp gore:  1.0 mi

Type B weave in segment:  No

EXERCISE 2:  FREEWAY SEGMENT (continued)

Traffic Data

Freeway Segment Data

AADT (year 2006):  88,000 veh/d

AADT (year 2014):  92,100 veh/d

Ramp Data

AADT (year 2006):  6,000 veh/d (all ramps)

AADT (year 2014):  6,100 veh/d (all ramps)

Crash Data

| Crash Type | Count |
| --- | --- |
|  | Fatal-and-injury | Property-damage-only |
| Multiple-vehicle | 1 | 2 |
| Single-vehicle | 1 | 3 |
| Ramp-entrance-related | 0 |
| Ramp-exit-related | 0 |
| Note: Counts can be entered for any years in the crash period (crash year is not used in ISAT). |

OUTPUT SUMMARY

What is the total expected number of crashes?  …………………………….

EXERCISE 3:  FREEWAY SEGMENT

Location:  Segment 3 on urban six-lane freeway section

Study period:  2013 to 2015				Area type: urban

Crash data description: Data for each individual segment

Crash period:  2005 to 2007

INPUT DATA

Basic Roadway Data

Number of lanes: 6

Segment length:  0.40 mi

Alignment Data

Horizontal curve in segment:  No

Cross Section Data

Lane width:  11 ft

Outside shoulder with:  6 ft

Inside shoulder width:  4 ft

Median width:  50 ft

Rumble strips on outside shoulders:  Yes, full length of segment

Rumble strips on inside shoulders:  Yes, full length of segment

Presence of barrier in median:  None

Roadside Data

Clear zone width:  15 ft

Presence of barrier on roadside:  Full (continuous)

Distance from edge of traveled way to barrier face (barrier offset):  8 ft

Ramp Access Data

Travel in Increasing Milepost Direction

Ramp entrance in segment:  No

Distance from begin milepost to upstream entrance ramp gore:  0.1 mi

Ramp exit in segment:  Lane drop

Type B weave in segment:  Yes

Length of weaving section:  0.5 mi

Length in segment:  0.4 mi

Travel in Decreasing Milepost Direction

Ramp entrance in segment:  Speed-change lane

Length of ramp entrance:  0.133 mi (= 700/5280)

Length of ramp entrance in segment:  0.133 mi

Ramp exit in segment:  Speed-change lane

Length of ramp exit:  0.066 mi (= 350/5280)

Length of ramp exit in segment:  0.066 mi

Type B weave in segment:  No

EXERCISE 3:  FREEWAY SEGMENT (continued)

Traffic Data

Freeway Segment Data

AADT (year 2006):  94,000 veh/d

AADT (year 2014):  98,200 veh/d

Ramp Data

AADT (year 2006):  6,000 veh/d (all ramps)

AADT (year 2014):  6,100 veh/d (all ramps)

Crash Data

| Crash Type | Count |
| --- | --- |
|  | Fatal-and-injury | Property-damage-only |
| Multiple-vehicle | 6 | 8 |
| Single-vehicle | 3 | 5 |
| Ramp-entrance-related | 1 | 2 |
| Ramp-exit-related | 0 | 0 |
| Note: Counts can be entered for any years in the crash period (crash year is not used in ISAT). |

OUTPUT SUMMARY

What is the total expected number of crashes?  …………………………….

EXERCISE 4:  FREEWAY SEGMENT

Location:  Segment 4 on urban six-lane freeway section

Study period:  2013 to 2015				Area type: urban

Crash data description: Data for each individual segment

Crash period:  2005 to 2007

INPUT DATA

Basic Roadway Data

Number of lanes: 6

Segment length:  0.20 mi

Alignment Data

Horizontal curve in segment:  No

Cross Section Data

Lane width:  11 ft

Outside shoulder with:  6 ft

Inside shoulder width:  4 ft

Median width:  50 ft

Rumble strips on outside shoulders:  Yes, full length of segment

Rumble strips on inside shoulders:  Yes, full length of segment

Presence of barrier in median:  None

Roadside Data

Clear zone width:  15 ft

Presence of barrier on roadside:  None

Ramp Access Data

Travel in Increasing Milepost Direction

Ramp entrance in segment:  No

Distance from begin milepost to upstream entrance ramp gore:  0.5 mi

Ramp exit in segment:  No

Distance from end milepost to downstream exit ramp gore:  0.8 mi

Type B weave in segment:  No

Travel in Decreasing Milepost Direction

Ramp entrance in segment:  No

Distance from end milepost to upstream entrance ramp gore:  0.8 mi

Ramp exit in segment:  No

Distance from begin milepost to downstream exit ramp gore:  0.4 mi

Type B weave in segment:  No

EXERCISE 4:  FREEWAY SEGMENT (continued)

Traffic Data

Freeway Segment Data

AADT (year 2006):  82,000 veh/d

AADT (year 2014):  86,000 veh/d

Ramp Data

AADT (year 2006):  6,000 veh/d (all ramps)

AADT (year 2014):  6,100 veh/d (all ramps)

Crash Data

| Crash Type | Count |
| --- | --- |
|  | Fatal-and-injury | Property-damage-only |
| Multiple-vehicle | 3 | 4 |
| Single-vehicle | 1 | 2 |
| Ramp-entrance-related | 0 |
| Ramp-exit-related | 0 |
| Note: Counts can be entered for any years in the crash period (crash year is not used in ISAT). |

OUTPUT SUMMARY

What is the total expected number of crashes?  …………………………….

EXERCISE 5:  FREEWAY SECTION

Location:  1.0-mile urban six-lane freeway section

Study period:  2013 to 2015

OUTPUT SUMMARY

What is the total expected number of crashes for the freeway section?  ….

What is the total expected number of crashes for the freeway section if

the cross section is changed for all four segments?  ………………………

Outside shoulder width:  7 ft

Inside shoulder width:  5 ft

Median width:  46 ft

Roadside barrier offset (segment 3):  9 ft

Note: these changes are proposed for (and applicable only to) the study period.

What is the total expected number of crashes for the freeway section if

the weaving section in segments 2 and 3 is changed to Type A?  …………………

Note: this change is proposed for (and applicable only to) the study period.

EXERCISE 6:  RAMP SEGMENT

Location:  Segment 1 (dashed line) on urban single-lane exit ramp

Study period:  2013 to 2015				Area type: urban

Crash data description: No crash data

INPUT DATA

Basic Roadway Data

Number of lanes: 1

Segment length:  0.22 mi

Average traffic speed on the freeway:  70 mi/h

Segment type: Exit

Type of control at crossroad ramp terminal:  Signal

Alignment Data

Horizontal curve:  In segment

Curve radius:  1,000 ft

Length of curve:  0.10 mi

Length of curve in segment:  0.10 mi

Ramp-mile of beginning of curve in direction of travel:  0.12

Cross Section Data

Lane width:  14 ft

Right shoulder with:  8 ft

Left shoulder width:  4 ft

Presence of lane add or lane drop:  No

Roadside Data

Presence of barrier on right side of roadway:  Yes

Length of barrier:  0.05 mi

Distance from edge of traveled way to barrier face (barrier offset):  8 ft

Presence of barrier on left side of roadway:  No

Ramp Access Data

Ramp entrance in segment:  No

Ramp exit in segment:  No

Traffic Data

AADT (year 2014):  6,100 veh/d

Crash Data

Not available

OUTPUT SUMMARY

What is the total predicted number of crashes?  …………………………...

EXERCISE 7:  RAMP SEGMENT

Location:  Segment 2 (solid line) on urban single-lane exit ramp

Study period:  2013 to 2015				Area type: urban

Crash data description: No crash data

INPUT DATA

Basic Roadway Data

Number of lanes: 1

Segment length:  0.10 mi

Average traffic speed on the freeway:  70 mi/h

Segment type: Exit

Type of control at crossroad ramp terminal:  Signal

Alignment Data

Horizontal curve 1:  Off segment

Curve radius:  1,000 ft

Length of curve:  0.10 mi

Length of curve in segment:  0.10 mi

Ramp-mile of beginning of curve in direction of travel:  0.12

Horizontal curve 2:  In segment

Curve radius:  500 ft

Length of curve:  0.05 mi

Length of curve in segment:  0.05 mi

Ramp-mile of beginning of curve in direction of travel:  0.25

Cross Section Data

Lane width:  15 ft

Right shoulder with:  8 ft

Left shoulder width:  4 ft

Presence of lane add or lane drop:  No

Roadside Data

Presence of barrier on right side of roadway:  No

Presence of barrier on left side of roadway:  No

Ramp Access Data

Ramp entrance in segment:  No

Ramp exit in segment:  No

Traffic Data

AADT (year 2014):  6,100 veh/d

Crash Data

Not available

OUTPUT SUMMARY

What is the total predicted number of crashes?  …………………………...

EXERCISE 8:  ENTIRE RAMP

Location:  0.32-mile urban single-lane exit ramp

Study period:  2013 to 2015

OUTPUT SUMMARY

What is the total predicted number of crashes for the entire ramp?  ….......

EXERCISE 9:  RAMP TERMINAL

Location:  Left-side terminal at urban interchange

Study period:  2013 to 2015				Area type: urban

Crash data description: No crash data

INPUT DATA

Basic Intersection Data

Ramp terminal configuration:  D4

Ramp terminal traffic control mode:  Signal

Presence of a non-ramp public street leg at the terminal:  No

Alignment Data

Distance to the next public street intersection on the outside crossroad leg:  0.25 mi

Distance to the adjacent ramp terminal:  0.17 mi

Traffic Control

Left-Turn Operational Mode

Protected-only mode on inside crossroad approach:  Yes

Right-Turn Control Mode

Right-turn control mode on exit ramp approach:  Yield

Cross Section Data

Crossroad median width:  12 ft

Number of Lanes

Both crossroad approaches:  4 lanes

Inside crossroad approach:  2 lanes

Exit ramp approach:  2 lanes

Right-Turn Channelization

Outside crossroad approach:  Yes

Exit ramp approach:  Yes

Left-Turn Lane or Bay

Presence of lane or bay on inside crossroad approach:  Yes

Width of lane or bay on inside crossroad approach:  12 ft

Right-Turn Lane or Bay

Presence of lane or bay on outside crossroad approach:  No

Access Data

Number of driveways on the outside crossroad leg:  1

EXERCISE 9:  RAMP TERMINAL (continued)

Traffic Data

Inside Crossroad Leg Data

AADT (year 2014):  7,500 veh/d

Outside Crossroad Leg Data

AADT (year 2014):  7,500 veh/d

Exit Ramp Data

AADT (year 2014):  5,000 veh/d

Entrance Ramp Data

AADT (year 2014):  5,000 veh/d

Crash Data

Not available

OUTPUT SUMMARY

What is the total predicted number of crashes?  …………………………...

EXERCISE 10:  RAMP TERMINAL

Location:  Right-side terminal at urban interchange

Study period:  2013 to 2015				Area type: urban

Crash data description: No crash data

INPUT DATA

Basic Intersection Data

Ramp terminal configuration:  A4

Ramp terminal traffic control mode:  One-way stop

Alignment Data

Exit ramp skew angle:  0 degrees

Distance to the next public street intersection on the outside crossroad leg:  0.25 mi

Distance to the adjacent ramp terminal:  0.17 mi

Traffic Control

Right-Turn Control Mode

Right-turn control mode on exit ramp approach:  Stop

Cross Section Data

Crossroad median width:  12 ft

Number of Lanes

Both crossroad approaches:  4 lanes

Exit ramp approach:  2 lanes

Right-Turn Lane or Bay

Presence of lane or bay on inside crossroad approach:  No

Presence of lane or bay on outside crossroad approach:  No

Traffic Data

Inside Crossroad Leg Data

AADT (year 2014):  7,500 veh/d

Outside Crossroad Leg Data

AADT (year 2014):  7,500 veh/d

Exit Ramp Data

AADT (year 2014):  2,500 veh/d

Entrance Ramp Data

AADT (year 2014):  1,250 veh/d

Crash Data

Not available

OUTPUT SUMMARY

What is the total predicted number of crashes?  …………………………...

EXERCISE 11:  INTERCHANGE TERMINALS

Location:  Two ramp terminals at an urban interchange

Study period:  2013 to 2015

OUTPUT SUMMARY

What is the total predicted number of crashes for both ramp terminals?  …

What is the total predicted number of crashes for both ramp terminals if

the driveway is closed?  …………………………………………………...

Freeway and Interchange Safety Evaluation Workshop

Workshop developed as part of NCHRP Project 17-45:

Enhanced Safety Prediction Methodology and Analysis Tool for Freeways and Interchanges

Date:

Location:

Your Agency:__________________________________________________________________

Your Position:__________________________________________________________________

Course Content  (circle one)

|  | Yes |  |  |  | No |
| --- | --- | --- | --- | --- | --- |
| 1. Did the course meet your expectations? Comments: __________________________________________________ __________________________________________________ | 1 | 2 | 3 | 4 | 5 |
| 2. Was the material presented at the correct level of difficulty? Comments: __________________________________________________ __________________________________________________ | 1 | 2 | 3 | 4 | 5 |
| 3. Was the topic of the course covered adequately (nothing left out, no one topic overemphasized)? Comments: __________________________________________________ __________________________________________________ | 1 | 2 | 3 | 4 | 5 |
| 4. Was the software easy to use? Comments: __________________________________________________ __________________________________________________ | 1 | 2 | 3 | 4 | 5 |

General Observations

5.	What did you like most about the course?

____________________________________________________________________________

____________________________________________________________________________

6.  What did you like the least about the course?

____________________________________________________________________________

____________________________________________________________________________

7.  What can we do to improve this workshop?

____________________________________________________________________________

____________________________________________________________________________

8.  Other Comments:

____________________________________________________________________________

____________________________________________________________________________

Thank you for taking the time to complete this course evaluation form.  Please make sure the course instructor receives it before you leave.