## Slide 1: NCHRP 22-26: Fatal and Serious Injury Factors in Motorcycle Collisions with Traffic Barriers
H. Clay Gabler
Virginia Tech
Department of Biomedical Engineering and Mechanics
Center for Injury Biomechanics

## Slide 2: NCHRP
The National Cooperative Highway Research Program (NCHRP) produces ready-to-implement solutions to the challenges facing transportation professionals. NCHRP is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; the FHWA; or NCHRP sponsors.

## Slide 3: Guardrail Fatalities by Vehicle Type
Motorcycles account for more guardrail fatalities than any other vehicle type
[Data from FARS 2018]
Motorcycles surpass all vehicles in Guardrail Fatalities

## Slide 4: NCHRP 22-26: Objective
What is the risk of serious-to-fatal injury in barrier crashes?
What are the causes of serious-to-fatal barrier injuries?
What are the countermeasures?

## Slide 5: Study 1: Relative fatality risk of fixed object vs. ground collisions

## Slide 6: Study 2: Does Injury Risk vary by Barrier Design?
2003 to 2008
3 States
951 Crashes
W-Beam Guardrail (NC)
W-Beam and Concrete Barrier
(NJ)
Cable Barrier (TX)
Photos from Google Earth
Barrier Type | New Jersey | North Carolina | Texas | Total
W-beam | 168 | 134 | 244 | 546
Concrete Barrier | 87 | 23 | 248 | 358
Cable Barrier | 0 | 15 | 32 | 47
Total | 255 | 172 | 524 | 951
Re: Daniello and Gabler (TRR, 2011)

## Slide 7: Injury Severity by Barrier Type Helmeted Riders

## Slide 8: Odds Ratio of Severe Injury (K+A) Helmeted Riders
W-Beam
vs.
Concrete Barrier
Cable Barrier
vs.
Concrete Barrier
Cable Barrier
vs.
W-Beam
No Statistical
Difference between
Cable and W-Beam Risk

## Slide 9: Study 3: Rider Trajectory vs. Injury
Problem:
  Riders often separate from motorcycle on impact
  Police accident reports indicate rider/motorcycle as united
  Do riders actually impact guardrail?
Research Questions
  How do riders impact barrier? Upright, sliding, other?
  How does rider trajectory influence injury risk?
Re: Daniello A, Cristino D, and Gabler HC, “Relationship Between Rider Trajectory and Injury Outcome in Motorcycle-Barrier Crashes”, Transportation Research Record (2013)
Approach:
  NJ 2007 – 2011
  342 MC-Barrier crashes categorized
  Compute odds of serious injury (K+A)

## Slide 10: Injury Risk vs. Upright

## Slide 11: Impact Configuration
Source | Upright Impact (%) | Sliding Impact (%)
Quincy et al. (1988) | 42 | 58
Berg et al. (2005) | 51 | 45
Peldschus et al. (2007)* | 75* | 25*
Baumbach et al. (2013) | 44 | 47
Daniello et al. (2013 | 51 | 41
*Note: Also included non-barrier run-off-road crashes
Only 8% of riders do not impact barrier
Impacts approx. split between upright & sliding
Source | Upright Impact (%) | Sliding Impact (%)
Quincy et al. (1988) | 42 | 58
Berg et al. (2005) | 51 | 45
Peldschus et al. (2007)* | 75* | 25*
Baumbach et al. (2013) | 44 | 47
Daniello et al. (2013 | 51 | 41

## Slide 12: Study 4: What Injuries Occur in Barrier Crashes?
1,707 motorcyclists in crashes in Maryland
  CODES: Linked Hospital + Police Accident Reports
Odds of thoracic injury double in barrier crashes
Need to differentiate between barrier types
Re: Daniello A and Gabler HC,
“The Characteristics of Injuries in Motorcycle to Barrier
Collisions in Maryland”,
Transportation Research Record (2012)
Serious Injuries (AIS3+)
Injuries indicate blunt impact, Not laceration

## Slide 13: Study 5: Effect of Roadway Characteristics on Injury
Research Question:
Do roadway characteristics affect risk of injury in barrier crashes?
  Radius of Curvature
  Vertical Grade
  Speed Limit
  Shoulder Width
  Traffic Volume
  Divided vs. Undivided
Data Sources:
Re: Gabauer DJ, “Characterization of roadway geometry associated with motorcycle crashes into longitudinal barriers,”
Journal of Transportation Safety and Security (2016)

## Slide 14: Injury Risk (K+A)
Variable Type | Parameter | Value | Comparison Group | Odds Ratio | 95% CI
Roadway | Normalized horizontal curve radius | < 820 feet | Tangent Section | 1.31 | 0.92 – 1.9
 |  | ≥ 820 feet | Tangent Section | 0.96 | 0.63 – 1.5
 | Vertical grade | < 3% | ≥ 3% | 1.28 | 0.95 – 1.7
 | Posted speed | > 45 mph | ≤ 45 mph | 1.32 | 0.97 – 1.8
 | Roadside shoulder width | ≥ 2 and < 10 feet | < 2 feet | 1.11 | 0.72 – 1.7
 |  | 10+ ft | < 2 feet | 0.91 | 0.53 – 1.6
 | AADT | < 2,500 vpd | > 50,000 vpd | 1.09 | 0.62 – 1.9
 |  | 2,500 – 9,999 vpd | > 50,000 vpd | 1.55 | 0.89 – 2.7
 |  | 10,000 – 49,000 vpd | > 50,000 vpd | 1.00 | 0.67 – 1.5
 | Configuration | Divided | Undivided | 1.81 | 1.16 – 2.8
Crash | Surface condition | Dry | Wet | 3.78 | 2.09 – 6.8
 |  | Other | Wet | 2.86 | 0.80 – 10.2
Rider | Helmet use | No | Yes | 2.04 | 1.56 – 2.7
 |  | Unknown | Yes | 1.45 | 0.81 – 2.6
 | Age | > 25 years | ≤ 25 years | 1.43 | 1.03 – 2.0
 | Alcohol | Yes | No | 2.99 | 2.10 – 4.3
No statistically significant difference
Higher Injury
Risk
Factors

## Slide 15: Study 6: What are the causes of Motorcycle-Barrier Injuries
Approach:
  In-depth crash investigations
  22 cases collected
Barrier Struck Distribution:
  18 W-beam
  2 Cable
  1 Cable + W-Beam
  1 Concrete + W-Beam

## Slide 16
Case MC-007-D:
Motorcycle:
2003 Harley Davidson
Electra Glide Classic
Barrier Struck
W-Beam
Rider
33 y.o. male
230+ lbs.

## Slide 17
Second Post Upstream from Impact Point
Fourth Post Upstream from Impact Point
Ebar End Cap
Displaced Post
Tissue Transfer
Case MC-007-D:

## Slide 18
Case Occupant Injuries

## Slide 19: Serious Injuries by Body Region and Source (MAIS 3+)
Thorax and Lower Extremities are nearly 2/3 of serious injuries
Body Region
Injury Source

## Slide 20: Conclusions
40% of guardrail fatalities are motorcyclists.
Fatality Risk from guardrail nearly double risk from concrete barrier.
No evidence that cable more dangerous than W-Beam.
Serious injuries are primarily to thorax and lower extremities.
Countermeasure priority – reduce post entanglement.

## Slide 21: Countermeasure Priorities
Rider entanglement with posts
Lacerations from top of posts
Laceration from top of rail
No evidence of wire rope laceration
Rider MC-007-D
dragged along top of posts
causing serious abdominal
injuries

## Slide 22: Example Countermeasures
Images – Lindsay, Sodirel,
EuroRAP, MCDonald, Ingal

## Slide 23: Pilot Tests of MPS in US
CALTRANS: 260 feet on canyon road near Auburn, CA. No impacts since installed.
NCDOT: 4500 feet on NC 143 installed in 2018. Will be evaluated in 2021.
Lindsay Transportation Systems
DR-46 Motorcycle Barrier Attenuator

## Slide 24: CEN TS 1317-8 Crash Testing in Europe
Configuration 1:
Post-Centered
for continuous and
discontinuous MPS
Configuration 2:
Post- Offset
only for
discontinuous MPS
Configuration 3:
Midspan
only for
continuous MPS
Currently, No Motorcycle Crash Test in MASH

## Slide 25: Opportunities to improve CEN 1317-8
Grzebieta et al. (2013) noted CEN 1317-8 does not test most common crash configurations and injuries.
Only tests sliding configuration. Upright impacts are approximately 50% of crashes.
Only evaluates head and neck injury. Most serious injuries are to thorax.
Is dummy biofidelic?

## Slide 26: Recommendations
Develop a MASH motorcyclist crash test
Considerations for the AASHTO Roadside Design Guide
Develop methods to determine where to locate Motorcycle Protection Systems (MPS)
Evaluate field performance of US pilot tests of Motorcyclist Protection Systems (CA and NC)
Evaluate EN 1317-8 crash test in the US
Evaluate crash performance of Motorcyclist Protection Systems for four-wheeled vehicles