## Slide 1: Proposed Guidance for Fixed Objects in the Roadside Design Guide NCHRP Project 17-82

## Slide 2
This slide presentation was developed by MRIGlobal under NCHRP Project 17-82. More information about this topic can be found in NCHRP Research Report 1016: Design Guidelines for Mitigating Collisions with Trees and Utility Poles on the National Academies Press website (www.nap.edu).
NCHRP is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; FHWA; or NCHRP sponsors.

## Slide 3: Background
18,000 traffic fatalities per year result from roadway departures
  Over 7,000 of these involve collisions with roadside fixed objects.
  Trees are the roadside fixed object most frequently involved in fatal crashes.
  The second type of roadside fixed object most commonly struck in fatal crashes are utility poles and light supports.
Given the scale of our roadway system, the diverse nature of existing roadsides, and the limited funds for safety improvement, not every roadside can be treated or mitigated to provide the full clear zone.
Highway agencies need to be able to establish priorities for roadside improvements.

## Slide 4: Research Objective
To develop design guidance for use by engineering practitioners to quantify the relative risk of collisions with roadside fixed objects.

## Slide 5: Research Focus
Fixed objects on the outside of the roadway (i.e., on the right side of the road on divided highways and on both sides of the road on undivided highways).
  Fixed objects in the median can be addressed through interpretation of the results for roadside fixed objects outside of the roadway(s).
Trees and utility poles on the following roadway types:
  Rural two-lane highways
  Rural multilane undivided highways
  Rural multilane divided highways

## Slide 6: Outline of Design Guidelines
Chapter 1 – Introduction
Chapter 2 – Design Criteria for Clear Zones
Chapter 3 – Crash Reduction Programs for Roadside Trees and Utility Poles
Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
Chapter 5 – Recommended Benefit-Cost Analysis Method
Chapter 6 – Benefit-Cost Analysis Examples
References
Appendix A – Recommended Crash Prediction Model for Tree- and Utility-Pole-Related Crashes
Appendix B – Predicting the Frequency and Severity of Tree- and Utility-Pole-Related Crashes with the Accompanying Spreadsheet Tool

## Slide 7: Chapter 1 – Introduction
Presents basic crash history data
  18,000 roadway departure fatalities per year
  7,000 roadside fixed-object fatalities per year
  3,500 fatalities per year involving roadside trees
  820 fatalities per year involving roadside utility poles and light supports
Explains role of roadside improvement program
References key role of the AASHTO RDG
Presents organization of remainder of design guidelines document

## Slide 8: Chapter 2 – Design Criteria for Clear Zones
Summarizes AASHTO RDG guidance on clear zones including suggested clear-zone distance and horizontal curve adjustment factors

## Slide 9: Chapter 3 – Crash Reduction Programs for Roadside Trees and Utility Poles
Roadside trees
  includes existing material about trees from RDG Section 4.9
  includes new material about trees from benefit-cost analysis examples (Chapter 5 of design guidelines)
Utility poles
  includes existing material about utility poles from RDG Section 4.8
  includes new material about utility poles from benefit-cost analysis examples (Chapter 5 of design guidelines)

## Slide 10: Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
Presents brief review of literature/existing models
Presents a new recommended crash prediction model developed in the research – a modified version of the Road Assessment Program (RAP) model:
  predicts annual frequency of fatality and injury (FI) crashes related to trees or utility poles
  applicable to rural two-lane undivided highways, rural four-lane undivided highways, rural four-lane divided highways (nonfreeways)

## Slide 11: Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
Safety Performance Functions (SPFs) consider:
  motor-vehicle traffic volume (AADT)
  number of objects on left and right sides of the road
    number of individual objects (trees or utility poles)
    length of continuous tree groups (converted to an equivalent number of individual trees)
  calibration factors for trees and utility poles (based on data collected and analyzed in this research)
Adjustment Factors (AFs):
  roadway design speed
  traffic flow influence factor
  median traversability factor
  crash likelihood factors
  crash severity factors

## Slide 12: Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
  Crash Likelihood Factors:
  lane width
  horizontal curvature
  advance visibility of curve
  percent grade
  presence of shoulder rumble strips
  presence of delineation
  road surface condition
  pavement skid resistance
  Crash Severity Factors:
  type of roadside object
  distance from traveled way to roadside object
  paved shoulder width

## Slide 13: Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
  Model Outputs
    predicted number of FI run-off-road tree-related (or utility-pole-related) crashes per year (NROR)
    predicted number of FI tree-related (or utility-pole-related) crashes per year by crash severity level:
      fatal (K-injury) crashes
      incapacitating injury (A-injury) crashes
      nonincapacitating injury (B-injury) crashes
      possible injury (C-injury) crashes
    predicted number of persons injured in tree-related (or utility-pole-related) crashes per year:
      persons with fatal injuries (K injuries)
      persons with incapacitating injuries (A injuries)
      persons with nonincapacitating injuries (B injuries)
      persons with possible injuries (C injuries)

## Slide 14: Chapter 4 – Relationship of Presence of Roadside Trees and Utility Poles to Crash Frequency and Severity
  Model predictions can be expressed as a crash modification factor (CMF):
  CMF = NROR for potential improved design / NROR for existing or planned design

## Slide 15: Chapter 5 – Benefit-Cost Analysis Method
Benefit-Cost Ratio: Benefits / Costs
Net Benefits: Benefits - Costs

## Slide 16: Chapter 5 – Benefit-Cost Analysis Method
Elements of Benefit-Cost Analysis Method
  annual number of crashes reduced
  crash costs by crash severity level (based on 2018 FHWA publication by Harmon et al.)
  improvement service life (default value: 20 years)
  discount rate or minimum attractive rate of return (default value: 7%)
  uniform series present worth factor
  present value of crash reduction benefits
  implementation cost for proposed improvement

## Slide 17: Chapter 6 – Benefit-Cost Analysis Examples
Computations illustrated for five (5) benefit-cost examples
All examples related to roadside fixed objects on rural two-lane undivided highways
Range of conditions considered:
  Two-way traffic volume (AADT) equal to 1,000, 5,000, and 10,000 veh/day
  Distance from traveled way to roadside object: 6, 10, 15, 20, 25, 30, 35, and 40 ft
Roadway characteristics for all examples
  70-mph design speed
  12-ft lanes, 6-ft paved shoulders
  Tangent alignment
  2% grade
  Good delineation, road surface condition, and pavement skid resistance

## Slide 18: Chapter 6 – Benefit-Cost Analysis Examples
Benefit-Cost Example #1 – Removal of an Isolated Roadside Tree
Removal of a single, isolated roadside tree on a rural two-lane highway

## Slide 19: Chapter 6 – Benefit-Cost Analysis Examples
Benefit-Cost Example #2 – Removal of an Continuous Tree Group
Removal of a continuous tree group, 0.5 miles in length, spaced at intervals of 5 ft, on a rural two-lane highway

## Slide 20: Chapter 6 – Benefit-Cost Analysis Examples
Benefit-Cost Example #3 – Relocation of a Single Utility Pole
Removal of a single utility pole on a rural two-lane highway

## Slide 21: Chapter 6 – Benefit-Cost Analysis Examples
Benefit-Cost Example #4 – Relocation of an Extended Series of Utility Poles
Relocation of a series of 9 utility poles spaced at 300-ft intervals over 0.5 miles of a rural two-lane highway

## Slide 22: Chapter 6 – Benefit-Cost Analysis Examples
Benefit-Cost Example #5 – Relocation of an Extended Series of Utility Poles and Replacement with Underground Utilities
Relocation of a series of 9 utility poles spaced at 300-ft intervals over 0.5 miles of a rural two-lane highway and replacement with underground utilities