## Slide 1
The following presentation is supplemental to NCHRP Research Report 1103: The Effect of Vehicle Mix on Crash Frequency and Crash Severity (NCHRP Project 22-49). The full report can be found by searching on the report title on the National Academies Press website (nap.nationalacademies.org).
The National Cooperative Highway Research Program (NCHRP) is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; the FHWA; or NCHRP sponsors.

## Slide 2: NCHRP Project 22-49 The Effect of Vehicle Mix on Crash Frequency and Crash Severity
Project Final Presentation
November 2023

## Slide 3: Project Team
Project Team | Team Members
 | Naveen Eluru (Principal Investigator) Mohamed Abdel-Aty Tanmoy Bhowmik Shahrior Pervaz Dewan Ashraful Parvez Lauren Hoover
 | Kai Wang (Co-Principal Investigator) Shanshan Zhao Manmohan Joshi John N. Ivan

## Slide 4: Outline
Future HSM Considerations
Project Background and Objectives
Project Tasks Completed
Key Project Deliverables
Project Implementation

## Slide 5: Project Background
Highway Safety Manual (HSM) provides methods and procedures in estimating crashes at different levels.
However, these methods currently do not account for the influence of vehicle mix information while model estimation.
Recent research efforts show a substantial impact of vehicle mix on crashes.
The incorporation of vehicle mix would improve crash predictive methods and assist in better use of the limited funds and resources.

## Slide 6: Project Background
The current project has
  explored the impact of vehicle mix on crash analysis.
  developed crash frequency and severity models for jurisdictions with vehicle mix data available by facility type.
  incorporated vehicle mix information in newer approaches.
The newer approaches proposed have the advantage of being developed for recently completed NCHRP research (17-85) and would naturally lend themselves to modifying the HSM model structure for future versions.

## Slide 7: Project Objectives (from RFP)
Develop methods to quantify the effect of vehicle mix on crash frequency and severity for various facility types
Develop a spreadsheet tool for practitioners to quantify the effect of vehicle mix on safety performance
Objective 1
Objective 2

## Slide 8: Project Tasks Completed
Phase I
Task 1: Prepare a technical report that summarizes literature review, data availability, analytical approaches and develops a framework for incorporating vehicle mix in frequency and severity models
Task 2: Develop a detailed work plan with data sources, selected facility types, data processing and analysis approaches, validation metrics and spreadsheet development
Task 3: Prepare and submit an interim report

## Slide 9: Project Tasks Completed
Phase II
Task 4: Apply the proposed framework by processing the data, estimating and validating models by facility type and examining model performance
Task 5: Develop a spreadsheet tool clearly outlining the methodology and application guidance
Task 6: Use practical examples, to test and illustrate the spreadsheet tool
Task 7: Prepare an instruction guide and a quick start guide for facilitating adoption of the developed models

## Slide 10: Project Tasks Completed
Phase II
Task 8: Provide a virtual demonstration for the NCHRP Panel as well as a final presentation to sponsoring committees including coordination with NCHRP and AASHTO Committee on Highway Traffic Safety
Task 9: Prepare an accessible report with guidelines for future HSM adoption
Task 10: Prepare draft final deliverables
Task 11: Prepare documentation and guidance summarizing the research effort, future research recommendations, spreadsheet tools to enhance state DOTs’ procedures for updating crash frequency and severity models and a TR News article

## Slide 11: Data Source
HSIS
California
Illinois
North Carolina
Ohio
Washington
Minnesota
Non-HSIS
Connecticut
Florida
Texas
South Dakota
Variables missing
Variables missing

## Slide 12: Facility Selection
First, the team focused on the facilities that are covered in the first edition of the HSM
  rural two-lane two-way roadways, rural multilane highways, urban/suburban arterials, freeway segments and intersections
Each facility is further categorized into multiple categories based on different variables (number of lanes, presence of median).
Estimating models for all the facilities will require substantial amount of time and effort
  Vehicle mix might not vary across locations
The research team focused on major facilities based on total and heavy vehicle crashes.

## Slide 13: Facility Selection (Coarser Level)
Segment Facilities
Urban
Limited Access Facilities
Arterials
Rural
Urban
Rural
Intersection
Facilities
Urban
Rural

## Slide 14: Facility Selection (Finer Level)
Segment Facilities
Urban
Limited Access Facilities
Arterials
Rural
Urban
Rural
Intersection
Facilities
Urban
Rural
3-leg STOP controlled
4-leg STOP controlled
3-leg signalized
4-leg signalized
4-lane divided
6-lane divided
8-lane divided
10-lane divided
2-lane undivided
3-lane
4-lane undivided
4-lane divided
5-lane
3-leg STOP controlled
4-leg STOP controlled
4-leg signalized
4-lane divided
6-lane divided
8-lane divided

## Slide 15: Facility Selection: Detailed Classification
Facility Type
Segment Facility
Intersection Facility
CA
CT
FL
IL
MN
TX
WA
CA
CT
FL
MN
Limited Access Facilities:
Urban 4-LD
Urban 6-LD
Urban 8-LD
Urban 10-LD
Rural 4-LD
Rural 6-LD
Rural 8-LD
Arterials:
Urban 2-LUD
Urban 3-L
Urban 4-LUD
Urban 4-LD
Urban 5-L
Rural 2-LUD
Rural 3-L
Rural 4-LUD
Rural 4-LD
Rural 5-L
STOP Controlled:
Urban 3-leg
Urban 4-leg
Rural 3-leg
Rural 4-leg
Signalized:
Urban 3-leg
Urban 4-leg
Rural 4-leg
24 Facilities

## Slide 16: Pooled Datasets
Pooled Data
California
Illinois
Washington
Florida
Connecticut
Minnesota
Texas
Facility Type
Estimation Sample
Repeat process by
facility type
Validation Sample

## Slide 17: Variable Assessment
Dependent Variables
  KABCO severity scale
    K (fatal crashes),
    A (incapacitating crashes),
    B (non-incapacitating crashes),
    C (possible injury crashes), and
    O (no injury crashes).
For intersection crashes - crashes that occurred within a 250ft intersection buffer are assigned.

## Slide 18: Variable Assessment
Independent Variables
  HSM aligned variables
    Roadway Characteristics
      Lane width, median width, shoulder width
    Traffic Characteristics
      AADT, major AADT, minor AADT
  New vehicle mix variables
    Coarser Level: %truck, %major road truck, %minor road truck
    Finer Level: %truck types (single unit, double unit etc.)

## Slide 19: Vehicle Mix Data Availability
State | Vehicle Mix Data Availability | Vehicle Classification |  | Data Used for Models | Source
 |  | Coarse | Fine |  | 
HSIS States |  |  |  |  | 
California | Available | Car | -- | Observed | CDOT
 |  | Truck | Two axle, three axle, four axle, five axle |  | 
Illinois | Available | Car | -- | Observed | IDOT
 |  | Truck | Single unit, multi-unit |  | 
Minnesota | Available | Car | -- | Observed | MNDOT
 |  | Truck | Single unit, combination unit truck |  | 
Washington | Available | Car | -- | Observed | WSDOT
 |  | Truck | Single unit, double unit and triple unit |  | 
Non-HSIS States |  |  |  |  | 
Connecticut | Not Available | Car | -- | Generated | QIE technique
 |  | Truck | -- |  | 
Florida | Available | Car | -- | Observed | FDOT
 |  | Truck | -- |  | 
Texas | Available | Car | -- | Observed | TXDOT
 |  | Truck | Single unit, combination truck |  | 

## Slide 20: Approach and Assumptions of Vehicle Mix Data
We employed state specific GIS data
  Developed approaches to match the nearest sections in GIS using proximity tools
When data for the exact crash year was not available, AADT data for the crash year was employed along with the truck percentage from the nearest years (with an upper limit of 2years) to get truck AADT
For jurisdictions without any Truck data, we employed Quasi-induced Exposure method to generate data (for Connecticut)

## Slide 21: Generating Vehicle Mix Data
For Connecticut, we do not have information on vehicle mix
We adopted the QIE approach to generate vehicle mix data
Basic Idea: Proportion of a driver/vehicle category not at fault in two- or more-vehicle collisions is related to the exposure of that driver/vehicle category in the entire driving population at the location
  We aggregated nearby sites to get a large sample to estimate the proportions
  It allows us to accommodate vehicle information purely relying on crash data
  Further, the relative appropriateness of the approach can be easily evaluated

## Slide 22: Model Estimation with Truck Data
Based on the data availability, we used following variables as vehicle mix data
  %truck: Truck AADT*100/AADT
  %SUT: Single unit truck AADT*100/AADT
  %major road truck: Truck AADT in major road*100/major road AADT
  %major road truck: Truck AADT in minor road*100/minor road AADT
To consider additional forms of truck traffic affecting crash counts
  We tested for the impact of trucks in locations with high truck volume
    These are locations with truck proportion >= 85th Percentile of truck traffic proportion for the facility type
    For Rural Arterial 2 Lane Undivided (RA2LUD) segments, the high truck 85th percentile value was 20%.

## Slide 23: Model Frameworks
HSM Model
Multivariate Poisson-lognormal Model
Negative Binomial- Ordered Probit Fractional Split Model
Test and finalize
SPF and SDF with
vehicle mix variables

## Slide 24: HSM Model
HSM models were estimated and used as benchmark for comparison of the newly developed model systems in terms of data fit and predictive ability.

## Slide 25: Multivariate Count Method
1
ID
1
2
3
4
Total Crash
10
12
8
4
PDO
6
6
5
0
Injury
4
5
2
3
Fatal
0
1
1
Crash counts
Develop Multivariate Poisson Log-normal (MVPLN) model
for crash severity levels
at each facility type
by severity level

## Slide 26: Count Fractional Split Method
NB
Model
1
ID
1
2
3
4
Total Crash
10
12
8
4
PDO
6
6
5
0
Injury
4
5
2
3
Fatal
0
1
1
PDO
0.6
0.5
0.63
0
Injury
0.4
0.42
0.25
Fatal
0
0.08
0.12
0.25
0.75
Ordered Fractional Split Model
Predicted
Severity Proportions
Predicted
Total Crash Counts
X
Predicted
Severity Counts

## Slide 27: Calibration of NB-OPFS Model
Models were developed considering 7 States for segment facilities (CA, CT, FL, IL, MN, TX, WA), and 4 States for intersection facilities (CA, CT, FL, MN)
Calibration is recommended for other states
Calibration factor for severity S,
Calibrated predicted crashes for severity S,
where = predicted number of crashes for severity level S

## Slide 28: Calibration of MVPLN Model
Models were developed considering 7 States for segment facilities (CA, CT, FL, IL, MN, TX, WA), and 4 States for intersection facilities (CA, CT, FL, MN)
Calibration is recommended for other states
Calibration factor for severity S,
Calibrated predicted crashes for severity S,
where = predicted number of crashes for severity level S

## Slide 29: Model Selection
Use of mean square error and predictive error
  We employed two different measures of fit:
    Mean Absolute Deviation (MAD)
    Mean Squared Prediction Error (MSPE)
where
= Predicted crashes,
= Observed crashes, at space i over a period of time.
The smaller the value, the better the model predicts observed crashes.

## Slide 30: Model Selection Process
For each facility type: 3 Models
  HSM
  Multivariate Poisson Lognormal
  Negative Binomial Fractional Split
For each model: 2 Performance measures
  MAD
  MSPE
MAD and MSPE
  2 samples: estimation and validation
  For all 5 severity (KABCO) categories
Identifying the “best” model is challenging
20 dimensions are compared (2*2*5)
It is unlikely: single model outperforms across all 20 measures

## Slide 31: Model Selection Process
Hence, we considered 2 approaches
  The first approach employs total crash frequency – model that performs better in predicting total crash counts for both samples (estimation and validation)
  The second approach employs a scoring process where the models that perform well for the severity levels are awarded a point and the score for each model across the severity levels is aggregated.
The final selection is considered based on 2 approaches

## Slide 32: Model Selection Process
Facility Group | Facility | Selected by MAD | Selected by MSPE | Selected for Facility | Recommended for Facility Group
Urban Limited Access | ULA4LD | NB-OPFS | NB-OPFS | NB-OPFS | HSM
 | ULA6LD | HSM | HSM | HSM | 
 | ULA8LD | HSM | HSM | HSM | 
 | ULA10LD | HSM | NB-OPFS/HSM | HSM | 
Rural Limited Access | RLA4LD | HSM | NB-OPFS/HSM | HSM | HSM
 | RLA6LD | HSM | HSM | HSM | 
 | RLA8LD | HSM | HSM | HSM | 
Urban Arterials | UA2LUD | NB-OPFS/HSM | NB-OPFS/MVPLN | NB-OPFS | NB-OPFS
 | UA3L | NB-OPFS/HSM | NB-OPFS/HSM | NB-OPFS/HSM | 
 | UA5L | NB-OPFS/HSM | NB-OPFS/HSM | HSM | 
 | UA4LUD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
 | UA4LD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
Rural Arterials | RA2LUD | NB-OPFS/MVPLN | NB-OPFS | NB-OPFS | NB-OPFS
 | RA3L | NB-OPFS | NB-OPFS | NB-OPFS | 
 | RA5L | MVPLN | NB-OPFS/MVPLN | MVPLN | 
 | RA4LUD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
 | RA4LD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
Scenario 1
Scenario 2
Scenario 3
If 2 different models are selected based on the 2 approaches, both models are considered.

## Slide 33: Model Selection for Facility Group
Facility Group | Facility | Selected by MAD | Selected by MSPE | Selected for Facility | Recommended for Facility Group
Urban Limited Access | ULA4LD | NB-OPFS | NB-OPFS | NB-OPFS | NB-OPFS
 | ULA6LD | HSM | HSM | HSM | HSM
 | ULA8LD | HSM | HSM | HSM | 
 | ULA10LD | HSM | NB-OPFS/HSM | HSM | 
Rural Limited Access | RLA4LD | HSM | NB-OPFS/HSM | HSM | HSM
 | RLA6LD | HSM | HSM | HSM | 
 | RLA8LD | HSM | HSM | HSM | 
Urban Arterials | UA2LUD | NB-OPFS/HSM | NB-OPFS/MVPLN | NB-OPFS | NB-OPFS
 | UA3L | NB-OPFS/HSM | NB-OPFS/HSM | NB-OPFS/HSM | 
 | UA5L | NB-OPFS/HSM | NB-OPFS/HSM | HSM | 
 | UA4LUD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
 | UA4LD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
Rural Arterials | RA2LUD | NB-OPFS/MVPLN | NB-OPFS | NB-OPFS | NB-OPFS
 | RA3L | NB-OPFS | NB-OPFS | NB-OPFS | 
 | RA5L | MVPLN | NB-OPFS/MVPLN | MVPLN | 
 | RA4LUD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 
 | RA4LD | NB-OPFS/HSM | NB-OPFS | NB-OPFS | 

## Slide 34: Model Selection for Facility Group
Facility Group | Facility | Selected by MAD | Selected by MSPE | Selected for Facility | Recommended for Facility Group
Urban Intersections | U3ST | NB-OPFS/MVPLN | NB-OPFS/MVPLN | NB-OPFS/MVPLN | MVPLN
 | U4ST | MVPLN | NB-OPFS/MVPLN | MVPLN | 
 | U3SG | MVPLN | MVPLN | MVPLN | 
 | U4SG | MVPLN | NB-OPFS/MVPLN | MVPLN | 
Rural Intersections | R3ST | NB-OPFS | NB-OPFS | NB-OPFS | NB-OPFS
 | R4ST | MVPLN | NB-OPFS/MVPLN | MVPLN | 
 | R4SG | NB-OPFS/MVPLN | NB-OPFS | NB-OPFS | 

## Slide 35: Model Recommendations for Segment Facilities
Facility Group | Facility | Recommended for Facility Group
Urban Limited Access | Urban 4-lane divided (ULA4LD) | NB-OPFS
 | Urban 6-lane divided (ULA6LD) | HSM
 | Urban 8-lane divided (ULA8LD) | HSM
 | Urban 10-lane divided (ULA10LD) | 
Rural Limited Access | Rural 4-lane divided (RLA4LD) | HSM
 | Rural 6-lane divided (RLA6LD) | 
 | Rural 8-lane divided (RLA8LD) | 
Urban Arterials | Urban 2-lane undivided (UA2LUD) | NB-OPFS
 | Urban 3-lane (UA3L) | 
 | Urban 5-lane (UA5L) | 
 | Urban 4-lane undivided (UA4LUD) | 
 | Urban 4-lane divided (UA4LD) | 
Rural Arterials | Rural 2-lane undivided (RA2LUD) | NB-OPFS
 | Rural 3-lane (RA3L) | 
 | Rural 5-lane (RA5L) | 
 | Rural 4-lane undivided (RA4LUD) | 
 | Rural 4-lane divided (RA4LD) | 

## Slide 36: Model Recommendations for Intersection Facilities
Facility Group | Facility | Recommended for Facility Group
Urban Intersections | Urban 3-leg STOP controlled (U3ST) | MVPLN
 | Urban 4-leg STOP controlled (U4ST) | 
 | Urban 3-leg signalized (U3SG) | 
 | Urban 4-leg signalized (U4SG) | 
Rural Intersections | Rural 3-leg STOP controlled (R3ST) | NB-OPFS
 | Rural 4-leg STOP controlled (R4ST) | 
 | Rural 4-leg signalized (R4SG) | 

## Slide 37: Final Report
Descriptive statistics/variable ranges of the facility
Model equations
Model estimation results
Model performance measures (Appendix)
Model estimation results with t-statistics (Appendix)
Elasticity (Appendix)
Chapter 6: Model Parameters

## Slide 38: Excel Spreadsheet Tools
To aid the practitioners in implementing the new models the research team developed three excel spreadsheet tools including:
  22-49 Spreadsheet Tool without Calibration,
  22-49 Spreadsheet Tool with Calibration, and
  22-49 Data Input and Prediction Tool

## Slide 39: Excel Spreadsheet Tools
22-49 Spreadsheet Tool without Calibration:
  Provides predictions for the user provided data directly without considering calibration.

## Slide 40: Excel Spreadsheet Tools
22-49 Spreadsheet Tool with Calibration:
  Provides predictions for the user provided data while modifying the predictions considering calibration.

## Slide 41: Excel Spreadsheet Tools
22-49 Data Input and Prediction Tool:
  Provides practitioners a tool to undertake crash frequency and severity analysis at a facility resolution (segment and intersection).

## Slide 42: Spreadsheet Tool User Guide
The step-by-step guidelines to use spreadsheet tools has been submitted.
Guidelines contains detailed instructions for three developed tools.

## Slide 43: Thank you