APPENDIX  D

ANALYSIS OF GENERIC SPANS FOR NON FORMULA B TRUCKS

This Appendix consists of the following sections:

- INTRODUCTION

- ANALYSIS OF GENERIC SPANS FOR CANDIDATE LOAD MODELS

- Representative non-Formula B Legal Trucks

- COMPARISON OF LOAD EFFECTS

Introduction

Survey findings reported in Chapter 2 indicate that a significant portion of the legal SHV population belongs in the category commonly referred to as “grandfather trucks”. They exceed FBF gross weight limits (( 80 K) and limits for axle groups. States such as PA, SC, and FL do not apply FBF to trucks weighing 73.28K or less on Interstate and other highways. Many more States either do not apply FBF or use a modified Bridge Formula to non-Interstate highways. The most common grandfathered truck seen in many States is the tri-axle dump truck that can weigh up to 75,000 pounds with a total wheelbase of less than 20 feet. They are legal under State law in some States with grandfather rights and are free to operate unrestricted, except as limited by bridge posting. Weight-limit posting for these vehicles seems to be the only safeguard the States have to protect their bridges from overstress or failure.

From the data set non Formula B trucks, certain trucks were identified as being the most severe in their class, based upon the excess load over the FBF limit (Table D-1).

TABLE D-1	More severe non-Formula B trucks

| DOT | Truck Designation | No of Axles | Total Spacing | Truck Weight (Kips) | FBF Limit for Gross Wt (K) | Excess Over FBF Limit (K) |
| --- | --- | --- | --- | --- | --- | --- |
| Delaware | DE 3 | 3 | 16.83 | 70.00 | 48.60 | 21.40 |
| Florida | SU3 | 3 | 15.17 | 66.00 | 47.40 | 18.60 |
| Connecticut | Construction Vehicle T4 | 4 | 18.20 | 76.50 | 54.10 | 22.40 |
| Delaware | DE 4 | 4 | 17.00 | 73.00 | 52.90 | 20.10 |
| Florida | SU4 | 4 | 18.34 | 70.00 | 53.70 | 16.30 |
| Pennsylvania | ML80 | 4 | 18.00 | 75.48 | 54.00 | 21.48 |

The heavier, more compact vehicles were selected for the analysis of load effects on the test suite of simple and continuous spans. This was done to minimize the computation effort associated with determining load effects. For the 3 axle dump trucks, Delaware DE3 and Florida SU3 were selected as the most severe. For the 4 axle dump trucks, Florida SU4, Connecticut T4, Delaware DE4, and Pennsylvania ML80 were selected (Fig D-1). Maximum moments and shears were calculated for the suite of simple and continuous span bridges with span ranges from 10 feet to 200 feet.  Bridges having transverse members were also included in this study. Floorbeam spacings from 10 feet to 30 feet in one-foot increments were included (Table D-10). The governing load models from the analysis of bridge spans are summarized in the tables given below.

Figure D-1  More Severe Non-Formula B Trucks

Analysis of Generic Spans FOR CANDIDATE LOAD MODLES

From Table D-5 It is evident that truck models Delaware DE3 (for 3 axle truck) and Connecticut T4 (for 4 axle trucks) impose the highest load effects in most longitudinal spans up to 200 ft (see Fig 12.2-1). For transverse beams with stringer spans from 10 ft to 30 foot, Connecticut T4 will govern live load reactions (Table D-10). The tables below show the spans for which these non-Formula B trucks govern over the Notional Rating Load NRL (developed in Phase I for Formula B trucks) and HS20 (truck or lane) loads. These trucks control mostly for the shorter spans. The controlling span ranges for moments and shears are as follows:

TABLE D-2 Governing span ranges

| Span Ranges Governed by DE3 and T4 |
| --- |
| Force Effect | DE3 | T4 |
| Simple Span Bending | 10’ to 40’ | 10’ to 95’ |
| Simple Span Shear | 10’ to 70’ | 10’ to 170’ |
| Two-Span Cont. Positive Bending | 10’ to 45’ | 10’ to 110’ |
| Two-Span Cont. Negative Bending | 10’ to 20’ | 10’ to 25’ |
| Two-Span Cont. Shear | 10’ to 55’ | 10’ to 110’ |
| Three-Span Cont. Positive Bending | 10’ to 40’ | 10’ to 100’ |
| Three-Span Cont. Negative Bending | 10’ | 10’ to 45’ |
| Three-Span Cont. Shear | 10’ to 50’ | 10’ to 100’ |
| Four-Span Cont. Positive Bending | 10’ to 40’ | 10’ to 95’ |
| Four-Span Cont. Negative Bending | --- | 10’ to 35’ |
| Four-Span Cont. Shear | 10’ to 50’ | 10’ to 100’ |

The moment ratios obtained by dividing the non-Formula B load effects by the NRL or HS20 load effects provide a quick metric of the degree of overstress in the various span configurations. The results are summarized in the table below. The overstress ratios ranged from 1.05 to 1.50 for DE3 and from 1.04 to 1.35 for T4 (Table D-3 and Tables D-6 thru D-9). This clearly demonstrates the significant overstress that will result from non-Formula B trucks in spans load rated using either HS20 or the NRL load model specified for Formula B vehicles. HS20 and NRL are therefore not suitable envelope load models for grandfathered trucks.

TABLE D-3 Maximum overstress ratios

| Maximum Overstress Ratios for Spans from 10 ft to 200 ft. |
| --- |
| Force Effect | Maximum Overstress Ratio = DE3 / NRL or HS20 | Maximum Overstress Ratio = T4 / NRL or HS20 |
| Simple Span Bending | 1.45 | 1.27 |
| Simple Span Shear | 1.47 | 1.29 |
| Two-Span Cont. Positive Bending | 1.50 | 1.28 |
| Two-Span Cont. Negative Bending | 1.11 | 1.25 |
| Two-Span Cont. Shear | 1.40 | 1.24 |
| Three-Span Cont. Positive Bending | 1.47 | 1.35 |
| Three-Span Cont. Negative Bending | 1.11 | 1.13 |
| Three-Span Cont. Shear | 1.42 | 1.33 |
| Four-Span Cont. Positive Bending | 1.46 | 1.33 |
| Four-Span Cont. Negative Bending | 1.05 | 1.04 |
| Four-Span Cont. Shear | 1.40 | 1.30 |

The HL-93 load model prescribed in the LRFD Specifications was defined such that the extreme load effects of the model are approximately the same as the exclusion trucks, which were taken to represent the extremes involved in present truck traffic (1993). This model consists of the design truck, design tandem, and the design lane, where the load effects of the design truck or the design tandem must be superimposed on the load effect of the design lane. As the HL-93 envelopes all exclusion traffic in the United States it can also serve as a screening load model for bridges that may be exposed to grandfathered trucks on a regular basis. The LRFR Manual requires that an initial check be performed based upon the HL-93 loading, in the same manner as was done in the MCE Manual for the HS20 loading. The main difference here is that the HL93 check will serve to identify bridges at risk from grandfathered loads whereas the HS20 rating is a check only for trucks that comply with federal weight laws. To further illustrate this point the DE3 and T4 truck moments were compared with HL93 moments, and as seen in Table D-4, the HL93 moments will envelope both these extreme trucks. Hence, HL93, a load model already familiar to many bridge engineers, should replace the NRL as a single envelope rating load model for bridges exposed to non-Formula B trucks.

TABLE D-4 Longitudinal moments compared with HL93

TABLE D-5    Governing load models for non-Formula B trucks

TABLE D-6 	Governing load effect ratios  -- simple spans

TABLE D-7   Governing load effect ratios  -- two span continuous

TABLE D-8	Governing load effect ratios  -- three span continuous

TABLE D-9   Governing load effect ratios -- four span continuous

TABLE D-10  	Live load reactions on transverse floorbeams

Representative non-Formula B Legal Trucks

Trucks DE3 and T4 are the most severe of the family of 3 and 4 axle grandfather loads. They can be used as representative of grandfather trucks, currently in use as state legal loads for rating and posting, for LRFR calibration and rating. The States can also use the calibrated load factor (L but apply a nominal loading based on their own non-Formula B truck. This will allow the states to post for their own grandfathered trucks by the LRFR process. Since there are many variations to federal weight law exclusions among the states, some flexibility in substituting state-specific grandfathered legal loads will be an important feature for national implementation. DE3 and T4 may be represented as two calibration trucks in the LRFR Manual that the states may use to benchmark their own vehicles.

Figure D-2  Governing non-Formula B trucks

COMPARISON OF LOAD EFFECTS

Comparison of Unfactored Moments

The unfactored moments (no impact) induced by these vehicles on longitudinal members are compared in Table D-11. As seen in the table below, the HL-93 serves as a reasonable envelope loading for the typical upper bound single-unit exclusion vehicles that are legal in the various states.

TABLE D-11 Unfactored Longitudinal Moments: HL-93 vs Exclusion Vehicles

Comparison of Factored Moments

Comparing factored load effects with impact will provide a more reliable measure of the variability in load ratings than the raw moments given above, as the distribution factor will be the same for all standard trucks. Table D-11 and Fig D-3 compare the factored HL-93 moments to the factored EX-3 and EX-4 moments for a site with an ADTT ≥ 5000. The moment ratios indicate that the factored HL-93 moments will exceed the factored exclusion truck moments at the Inventory level. Thus, if HL-93 has a RF ≥ 1.0 the bridge will have sufficient capacity for the EX-3 and EX-4 trucks. This validates the LRFR rating guideline based on using HL-93 as a first level screening check. LRFR A6.1.7.1 states that the design load rating can serve as a screening process to identify bridges that should be load rated for legal loads. Bridges that pass the design load check (RF ≥ 1) at the Inventory level will have satisfactory load rating for all legal loads.

Figure D-3 Ratios of Factored Longitudinal Moments HL-93 vs EX  Trucks

TABLE D-12  Ratios of Factored Longitudinal Moments HL-93 vs EX Trucks