APPENDIX  E

Estimating the Expected Maximum Load of Side-by-side Events by Simulation

This Appendix consists of the following sections:

- INTRODUCTION

- BACKGROUND

## Illustration: Analysis Of Ohio WIM Data

- Monte Carlo Simulation For Maximum Load Effect

- Conclusions

Introduction

As discussed in Section 3.3, the calibration of the LRFR live load factors requires the determination of the maximum expected live load over the evaluation period, denoted as Lmax. The calibration steps used a simplified statistical projection given in Eqn. 2. A Monte Carlo simulation was performed by Dr. Ghosn to validate the approach used during the course of this study to project the existing WIM data and estimate the expected maximum load effect for two side-by-side Short Heavy Vehicles (SHV). Simulation uses raw truck data collected on site and avoids the need to perform the fitting of the tail of the raw data through Normal distributions, which requires an iterative trial and error process. Simulation results demonstrated the validity of the projection approach used by Dr. Moses in the calibration.  The simulation approach can be used for short return periods, e.g. two years or less, when the number of side-by-side events is relatively small compared to the sample size of the available WIM database. For longer return periods, e.g. 75 years, or for large numbers of side-by-side events, a probability fit would still be needed but it can be executed based on the simulated data. This would reduce the level of subjectivity and lead to more uniform results.

# Background

The calibration of the load factors for SHV has been performed by Dr. Moses during the course of this study following steps consistent with the approach used by Nowak (NCHRP 368) during the calibration of the AASHTO LRFD specifications. The steps followed by Dr. Moses consisted of the following:

- Obtain raw WIM data from particular sites for the gross weights and axle configurations of the various truck configurations of interest.

- Send each truck data through an influence line to obtain the maximum moment response of each truck for a given span length.

- Plot the heaviest 20% of the data on Normal Probability curve.

- The data would typically not fit a Normal distribution except for the data that falls close to the tail end.

- By trial and error, truncate the data to determine the upper portion that best fits a Normal distribution. In our previous effort, the trial and error process consisted of the set of data that is most likely to fit a straight line on the Normal probability curve where the ordinate’s scale is adjusted to reflect the standard normal distribution.  The adequacy of the fit was determined by ensuring that the regression line through these data points produces a regression coefficient R2 on the order of 0.97 or higher.

- Determine the mean,, and the standard deviation, (x, for the Normal distribution that best models the tail end of the truncated data.

- Find the mean value of 2 side-by-side trucks assuming that the weights of the trucks in the main lane and those in the passing lane belong to the same population.  In this case, the mean of the load effect of 2 side-by-side trucks is:

(1)

The same population assumption can be relaxed if the weight data from different lanes show different statistics.

- Assuming independence and assuming the same truck weight population in the two lanes, find the standard deviation of the 2 side-by-side events as:

(2)

The assumption of independence can be relaxed if there is sufficient evidence Showing that the weights of the trucks in the passing lane are correlated to those in the main lane.

- Estimate the number of side-by-side events.  For SHV trucks, Dr. Moses estimated the number of side-by-side SHV trucks using an approach consistent with that used by Nowak during the LRFD calibration.  He assumed that a bridge site is exposed to a total ADTT=5000.  He also assumed that 500 SHV trucks cross a bridge site per day.  Out of the 5000 trucks 20% or 1000 trucks per day are heavy trucks.  The 20% heaviest SHV’s would constitute 100 SHV’s.  Following Nowak’s work, it is assumed that side-by-side events occur once every 15 crossings of trucks (6.7% of the total truck crossings are side-by-side).   Hence the total number of side-by-side events in a day is:  1000*(1/15)=66.7 trucks.  Moses also assumed that that the number of side-by-side events is proportionally to the truck traffic intensity.  Hence the number of side-by-side events for the population of 500 SHV’s is 0.667% leading to a total number of side-by-side SHV events to be 100*0.667%=0.667 per day.  In a two-year period the umber of SHV’s side-by-side becomes 487.

- Please note that the above estimate of 487 SHV’s side-by-side is extrapolated from the Nowak model, which was based on limited visual estimation of side-by-side events and originally looked at only regular truck traffic.  Current WIM data is being collected to include truck weights, truck types as well as headway information (i.e. number of side-bys-side events) for general truck traffic and SHV traffic.  Thus, with the WIM data currently being collected by Dr. Fu, better estimates of the number of side-by-side truck events and number of side-by-side SHV’s will be possible.  It is also observed that preliminary results collected by Dr. Fu confirm that the 6.7% assumption of heavy side-by-side trucks made by Nowak is overly conservative.  Current WIM data is showing that the number of side-by-side events is as low as 1% for all truck traffic.  Previous studies by Moses and Ghosn have shown less than 2-3% side-by-side events when the truck traffic was around 2000 trucks per day.

- Assuming an expected 487 SHV side-by-side events in a two-year return period, the maximum load effect expected in two years is given by:

(3)

where t=2.87 is the standard deviate corresponding to a probability of exceedance, pex=1/487.  Of course, when the new WIM data is made available, better estimates of the number of side-by-side events will be obtained and the value of Normal deviate, t, of Equation (3) can be changed accordingly.

## Illustration: Analysis Of Ohio WIM Data

The projection of the Ohio WIM data made available from the FHWA database is used herein to illustrate the process described in the previous section. The Ohio WIM data for SHV vehicles with 4 or more axles showed that there were 1530 such vehicles during the 31-day period when the data was collected. The heaviest 20% of these trucks constitute a total of 306 SHVs.  These vehicles were sent though influence lines for maximum moments of 20-ft, 40-ft and 60-ft simple spans. Out of the moments thus collected, the moments of the vehicles that produced moment effects higher than the legal limits were assembled into the three histograms shown in Figures E-1, E-2 and E-3.

Figure E-1. Histogram of 20-ft moments

Figure E-2. Histogram of 40-ft moments

Figure E-3. Histogram of 60-ft moments

The same data for the moments exceeding the legal limits is also plotted on Normal probability curves as shown in Figure E-4, E-5 and E-6 for the three different span lengths.  By trial and error the best-fit straight line that produces a regression coefficient R2 close to 0.99 through the upper tail of each set of data is obtained.  The three equations are shown in each figure where y is the standard normal deviate and x is the moment in kip-ft.  Notice that some of the extreme data points in each of the graphs were removed from the regression analysis to obtain a better fit.  There is a possibility that these data points represent outliers that would bias the results if included.

The intersection of the regression line with the abscissa indicates the value of the average moment of the equivalent Normal distribution that will best reproduce the tail end of the data.  The intersection of the line with a horizontal line drawn through the standard deviate = 1.0 will provide the value of the mean + 1 standard deviation of the equivalent Normal distribution. Accordingly, the means and the standard deviations of the equivalent Normal distributions that would best fit the tail end of the moments produced by the WIM data for the three spans are provided in Table E-1.

Figure E-4. Normal probability plot for moments of 20-ft spans

Figure E-5. Normal probability plot for moments of 40-ft spans

Figure E-6. Normal probability plot for moments of 60-ft spans

### Table E-1. Means and standard deviations of equivalent normal distribution

| Span Length | Mean moment of single truck load effect , (kip-ft) | Standard dev. of single truck load effect x, (kip-ft) | Mean moment of side-by-side effect , (kip-ft) | Standard dev. of side-by-side effects, (kip-ft) | Expected maximum of two-year period |
| --- | --- | --- | --- | --- | --- |
| 20-ft | 178.3 | 30.2 | 356.6 | 42.7 | 479.1 |
| 40-ft | 409.8 | 90.1 | 819.6 | 127.4 | 1185. |
| 60-ft | 719.8 | 142.9 | 1440. | 202.1 | 2020. |

By applying Equations 1 and 2, the mean and standard deviation of the moment effect of a side-by-side event is provided in the third and fourth columns of Table E-1.  Table E-1 also shows the expected maximum two-year load effect as calculated using equation 3 and a standard deviate t = 2.87.

Monte Carlo Simulation For Maximum Load Effect

The approach described above yields good results assuming that the fit on the tail of the histograms is reasonable.  A fit is especially needed to project the available data beyond the limited number of sample points that can be collected within a reasonable time period.  The issue that arises with the fit executed in Figures E-4 through E-6 is how to determine which data points should be used in the regression fit that is executed on the Normal probability scale. An alternative approach is to use a simulation to obtain the maximum load effect observed over a short period of time the results of which can be used as the bases for projections over longer periods of time. The process can be executed as described in Figure E-7 using the following steps:

- Assemble the data representing the moment effects for the trucks in the main lane into a histogram labeled Bin I in Figure E-7.

- Assemble the data representing the moment effects for the trucks in the passing lane into a histogram labeled Bin II in Figure E-7.

- Determine a main return period, treturn, for which the expected maximum moment is desired (e.g. a one week period, a month-period, a two-year period, or a 75-year period).  The basic period should be small enough so that the number of side-by-side events expected in this period is significantly smaller than the number of sample points that were used to create the histograms in Bin I and Bin II.  For example, in the simulation used in this example, the total number of trucks in the sample was = 1530 trucks out of which 487 samples were extracted for a basic return period of 2 years. The higher the number of data sample available to the number of data points extracted, the better will the results be.  It is most important to ensure that the simulation would not lead to reaching the maximum weight in the original histogram.  When this is observed to occur, then the basic return period should be decreased.   A projection to the final return period can be made as explained in Equations (4) and (5).

- Use a random number generator to randomly choose one truck from Bin I.

- Use a random number generator to randomly choose one truck from Bin II.

- Add the moment effects of these two trucks to produce the moment effect of a single side-by-side event.

- Repeat the process n times where n=number of side-by-side events expected in the basic return period treturn.

- Compare all the n moment effects and take the maximum value out of these n values.  This will produce a single estimate of Lmax,t.

- Repeat the whole simulation process m times to get m estimates of Lmax,t.

- Draw the histogram of the m estimates of Lmax,t and plot these values on a Normal Probability curve.

- Obtain the average value, and the standard deviation, , of Lmax,t.

- If the return period treturn is equal to the final period, T, for which the maximum value is desired, then the maximum expected value that should be used to calibrate the live load factor for SHV vehicles is Lmax=.

- Otherwise, if treturn<T, then use the probability plots and the histogram for Lmax,t to determine the most appropriate probability distribution that models Lmax,t. Experimentation with some data has shown that Lmax,t is likely to follow either a Normal distribution or an extreme type distribution (Gumbel).  In such cases. The maximum load effect can be calculated from either of the following two equations:

Lmax,t follows a normal distribution:

(4)

Lmax,t follows an extreme type distribution:

(5)

- In equation (6), i= T/treturn gives the number of repetitions necessary to obtain the total number of events expected in the total time period, T, as compared to the basic time period treturn.  The constant ( is the ratio of the circumference to the diameter of a circle = 3.14159.  In equation (4), ti = standard deviate for the probability of exceedance corresponding to the number of repetitions Prepetitions=1/i.

Figure E-7. Schematic representation of the Monte Carlo simulation

for side-by-side load effects

The process described in the previous steps was executed for the Ohio WIM data obtained from FHWA assuming that the number of side-by-side SHV loading events expected in a two-year return period is 487.  This is the same number of events that led to the standard deviate t = 2.87 that was used by Dr. Moses during his calibration of the live load factors.  The probability curves obtained for this two-year period for the moment effects for the 20-ft, 40-ft and 60-ft spans are provided in Figures E-8, E-9 and E-10 respectively. When the new headway data being assembled will be made available, the same process cane be repeated by using the actual number of side-by-side events rather than the estimated value of 487.

Figure E-8. Normal Probability for the two-year maximum moment for 20-ft spans

Figure E-9. Normal Probability for the two-year maximum moment for 40-ft spans

Figure E-10. Normal Probability for the two-year maximum moment for 60-ft spans

The data shown in Figures E-8, E-9 and E-10 demonstrates that the maximum two-year load effect for the 20-ft, 40-ft and 60-ft moments can be well represented by Normal distributions with the following mean values: 480.8 kip-ft, 1187 kip-ft and 1996 kip-ft respectively.  Notice that these values compare very well with the results given in Table E-1, which are 479 kip-ft, 1185-kip-ft and 2020 kip-ft respectively, showing a difference of less than 1% in all three cases.  If the projection for the 75-year period is desired, then equation 4 can be used with a number of repetitions i = 75/2 = 37.5 producing a ti = 1.93 along with the standard deviations 12.17, 33.75 and 46.68 for the 20-ft, 40-ft and 60-ft spans respectively.

The distributions observed in Figures E-8, E-9 and E-10 can be well represented using Normal distributions showing that most of the data fits within the 95% confidence limits (dashed lines in the figures) on the Normal Probability curve. However, if the number of repetitions is much higher than that used in these calculations (i.e. much higher than the 487 expected SHV side-by-side cases in a two-year return period), then it is more likely that the maximum load effect would follow a Gumbel Type I distribution. This would be true if the following assumptions are valid:

- The underlying distribution of truck weights is unlimited.

- The upper tail of the underlying distribution falls off in an exponential manner.

Then, it can be proven that the largest value of many independent variables taken from the distributions obeying the above conditions will approach a Gumbel Type I extreme value distribution. (see Benjamin & Cornell; 1970).

Notice that by applying equation (4) to get the 75-year maximum for the 20-ft span, the maximum load effect would be Lmax= 504 kip-ft.  The 40-ft and 60-ft spans would produce 1252 kip-ft and 2086 kip-ft respectively.  The application of Equation (5) would produce the following moment effects: 515 kip-ft, 1283 kip-ft and 2128 kip-ft for the maximum 75 year moment effect on the 20-ft, 40-ft and 60-ft spans respectively.  The small differences observed in the maximum load effects indicate that errors in determining the distribution types of Lmax,t do not significantly affect the final results. The low differences (less than 2%) are due to the low standard deviations max,t values obtained as the number of repetitions increases.   It is noted that the standard deviation after simulations will also be significantly lower than the original standard deviation of the truck weights.  For example, the raw truck data shows that the standard deviation of the upper 20% of the 20-ft span moment was approximately 17% (30.2/178.3) of the mean value.  After simulation this value was reduced to 2.5% (12.17/479).  Hence the differences between the results of equations (4) and (5) are expected to remain small.  In the event, where the standard deviations are large enough to make a significant difference, then a proper statistical analysis of the results of the simulation for the basic return period can be made to identify the probability distribution type that best fits the data.  Such methods may include Chi-Squared or Kolmogorov-Smirnov goodness of fit tests.  Subsequently, the projection for longer periods can be made using either Equation 4 or 5 whichever is deemed more appropriate or using similar equations that can be developed for other distributions types such as Log-Normal or Weibull probability distributions.

Conclusions

A Monte Carlo simulation has been used to verify the results of the analyses that led to the calibration of the live load factors for Formula B SHV vehicles.  The simulation demonstrated the validity of the model previously used in this study. Both approaches led to results that fall within 1% emphasizing the robustness of the approach.  The simulation process described in this section is valid as long as the basic return period produces a relatively low number of load repetitions that does not lead to simulated values from each of the bins of Figure E-7 that would consistently give the maximum value of the WIM histograms. The advantage of the simulation lies in avoiding the need to use trial and error to find the best fit for the original data plotted in Figures E-4, E-5 and E-6. Another advantage is the flexibility that the simulation would provide allowing for the consideration of various combinations of side-by-side and single lane events in the simulation including three or more lanes of traffic and trucks following each other in the same lanes.  The latter cases may be important for bridges having continuous spans. Also, the simulation process would allow the inclusion of various other random variables including load distribution factors and dynamic amplification factors if the need to include these variables arises.

# Text boxes

Truck in Lane 1

Truck in Lane 2

Bin I

Bin II