## Slide 1: NCHRP 20-101: Extreme Weather and Climate Change
Guidelines to Incorporate the Costs and Benefits of Adaptation Measures in Preparation for Extreme Weather Events and Climate Change

## Slide 2: Agenda
Executive Summary
Project Overview
Summary of Phase I Tasks
  Desktop research
  Gap Analysis
  Framework and Architecture Development
  Recommendations to Close Gaps
Summary of Phase II Tasks
  Level 1 Analysis Example
  Level 2 Analysis Example
Recommendations for Future Research

## Slide 3: Executive Summary
The transportation systems that provide essential support to our social and economic growth are increasingly stressed by extreme weather events and climate change
Additional demands placed on already-thin DOT budgets necessitate methods for prioritizing actions
CBA is one tool decision-makers can use to evaluate if and how to incorporate climate adaptation approaches into projects
Transportation practitioners perceive current CBA methods to be complex and time-consuming, so typically complete them only when required to do so
Because of their reluctance to complete CBAs, DOTs need a streamlined approach that incorporates climate change, multi-hazard mitigation, capital planning, and operations and management, while also using familiar inputs so that CBA is perceived as useful

## Slide 4: Executive Summary
Phase II framework options considered included:
  Sketch-Level framework that minimizes the number of inputs required and provides an order-of-magnitude CBA; should reduce barrier of entry for most DOTs to perform CBAs
  Climate Resilience framework requires some additional data and cost estimates for adaptation projects being considered to provide a benefit-cost ratio (BCR). Still useful for a majority of DOTs.
  Engineering Resilience framework provides CBA at the engineering design level. Requires additional data. Could be used to secure grant funding. Likely would be used only by advanced DOTs working on climate and weather resilience.
Phase II outcomes: Guidebook for Sketch Level (Study Level 1) and Climate Resilience CBA (Study Level 2) for flood hazards; Final Report
The Guidebook includes simplified approaches to conducting two levels of analysis (Screening and Net Present Value) to evaluate proposed projects, programs, and plans affected by extreme weather and climate change

## Slide 5: Project Overview
Problem Statement
“Extreme weather events and a changing climate can result in significant costs to transportation agencies…Research is needed to assist in an understanding of the cost/benefit payoff of adaptation measures to allow for better decision making.”
NOAA National Centers for Environmental Information (NCEI) U.S. Billion-Dollar Weather and Climate Disasters (2016). https://www.ncdc.noaa.gov/billions/
2011-2016 billion-dollar weather disasters by state
  Weather disasters are becoming costlier
  The Eastern U.S. is expected to get wetter
  Most of the U.S. is expected to get hotter
  The failure of government entities to prepare for climate change could affect credit ratings
  Decisions need to be made to (a) protect operational integrity; (b) minimize asset damage; or (c) strategically disinvest/sacrifice assets

## Slide 6: Summary of Tasks and Deliverables

## Slide 7: Task 1 - Synthesis
Cost-benefit frameworks evaluated include:
Climate change
Multi-hazard mitigation
Transportation Operations
Capital Planning
Effective practice examples:
MnDOT – Flash Flood Climate Adaptation Project (culverts)
DelDOT – Risk assessment using Hazus-MH; freeboard and wind parameters for bridges
CalTrans – CBAs for multi-modal transportation
Notes: TAM tools and VAST help prioritize assets and corridors for further analysis.
CBA tools like Cal B/C, COAST, etc., are available but are not sufficient to incorporate analysis of climate adaptation into the analysis

## Slide 8: Task 2 – Interviews and Outreach
Process: Interviewed 8 DOTs to gain additional insights | 
DOT Comments and Requests | Findings
DOTs increasingly are considering extreme weather and climate change in project selection and design Example: MSHA is moving toward integrated approach to planning, asset management, and climate change CBAs are typically completed only if policy requires it Perceived as time-consuming and expensive Hazard projections are difficult to assess Limit new data collection requirements: Need tools that leverage existing processes and data | Many DOTs have completed vulnerability assessments but have not applied CBA to them Much of the data needed for CBAs are available but it is often dispersed between agencies and across DOT branches Tools are lacking that consider CBA for a multi-hazard, multi-asset approach to adaptation that incorporates capital and operational considerations
Notes: Desire to strike a balance between abilities of DOTs with respect to CC and CBA. Might be able to design framework/model to accommodate different levels of analysis (through use of default values that allow for user input)

## Slide 9
“Low Regrets” Sketch-Level Resilience Analysis Framework
Climate Resilience Framework
Detailed Engineering Resilience Analysis Framework
[Hybrid of these Options]
Balance ease-of-use with the need for effective valuation framework
Task 3 - Summary of Framework Options
Least detailed
Simplified inputs
Limited, basic CBA
Most detailed
Demanding input requirements
Robust CBA
Moderate detail
Supports analysis of investments at different scales
Notes: Desire to strike a balance between abilities of DOTs with respect to CC and CBA. Might be able to design framework/model to accommodate different levels of analysis (through use of default values that allow for user input)

## Slide 10: Task 4 - Findings and Recommendations
The availability of multi-asset, multi-hazard, transportation-specific climate resilience CBA analysis tools are minimal.
Available Methods
Data and Inputs
Projects and Programs
Framework Options
A major framework design challenge is accommodating the range of available data and ease of organization-wide data sharing.
CBAs will be used to support multi-objective investments.
The research team recommended that the Climate Resilience framework be developed along with a prototype tool.

## Slide 11: Task 5 - Interim Meeting
The panel for this project requested that two CBA framework options be developed:
Study Level 1: Sketch-level
Study Level 2: Climate resilience level
No accompanying tool (just the methodology)

## Slide 12: Task 6 – Framework Development
Follows FHWA HEC-17 approach
Assumes that the level of damages associated with an event of a given magnitude will remain the same
Assumes return period for the event will decrease (i.e., become more frequent) due to climate change impacts
Analysis levels:
  Study Level 1 analysis uses three sets of data points and interpolates between them to estimate a threshold value for cost-effective adaptation
  Study Level 2 analysis adds data points to provide greater level of accuracy; adds benefit-cost ratio

## Slide 13: Study Level 1 Analysis Summary
Result: Provides the net present value of an incremental cost below which adaption is likely to be cost-effective.
Existing Conditions
Identify three return periods
  Tcnd: Largest return period with no damages under current conditions (Design Flow).
  Tcmod: Return period with moderate structural damages, riprap displacement and scour, and/or roadway flooding and traffic interruption.
  Tcmax: : Largest return period considered; possible bridge structural failure, road embankment erosion, loss of roadway function for weeks to months.
Associate flood flows and corresponding damages with each return period.
Calculate total annualized damages and multiply by the present value interest factor for the selected discount rate and project useful life to get total damages under current climate conditions.

## Slide 14
Study Level 1 Analysis Summary
Future Conditions
Estimate future flows under climate change conditions over project useful life for the three return periods (using, e.g., SWMM-CAT or SimCLIM)
Using known return periods and future flows, interpolate a new, climate-adjusted return period for the original (i.e., current condition) no-damage flow rate
Use current condition damages and flows to interpolate damages for climate-adjusted future flows
Calculate annualized damages for climate-adjusted future flows
Add annualized damages and multiply by present value interest factor to get total damages under climate change conditions
The total damages calculated for climate change conditions are used as the basis for evaluating cost-effectiveness of adaptation projects; adaptation project costing less than or equal to the value of the total damages are likely to be cost-effective

## Slide 15: Study Level 2 Analysis Summary
Result: Calculates the Benefit-Cost Ratio (BCR) for an adaptation project under climate change conditions.
Builds on Study Level 1 analysis:
  Interpolates additional frequency-damage points using climate-adapted return periods for current flow rates to render more accurate damage calculations
  Input adaptation project initial cost and annual operation & maintenance cost
  Evaluates the Benefit-Cost Ratio (BCR) for an adaptation project under climate change conditions.
Project 1
BCR
Total Project Costs
Project 2
BCR
Total Project Costs
Loss Estimates
Loss Estimates
Study Level 1 and Study Level 2 Analyses provide a basic and more detailed way, respectively, for DOTs to compare projects or programs impacted by extreme weather.

## Slide 16: Analysis Data Needs and Sources
Flood flows (or tide elevations for sea level rise analyses) associated with each return period
  H&H studies
  Flood Insurance Studies
  Past event data
Damages associated with each return period and corresponding flow
  Historic events
  Engineering estimates
  FEMA project worksheets
  Bid documents for construction
Discount rate
  OMB-recommended values of 3% and/or 7%
  Other values will be used consistent with financing mechanisms, policies, etc.
  Present value interest factor for selected discount rate(s) and project useful life
  Optional: sensitivity analysis comparing discount rates
Project Useful Life
  Anticipated length of time the project will be in place and used

## Slide 17: Task 7 – Guidebook and Final Report
Guidebook developed to assist decision makers to understand why and when to consider adaptation
Contents:
  Economic factors in a CBA
  Climate change considerations
  Typical costs and benefits included in CBAs for natural hazard events
  Detailed examples of Study Level 1 and Study Level 2 analyses

## Slide 18: Task 7 – Guidebook: When to consider adaptation
  Agency and funding requirements
  Likelihood of event occurrence
  Severity of consequences if the event occurs
  The useful life of the asset/project
  Select a scenario consistent with the acceptable level of risk and project timeframe

## Slide 19: Task 7 – Guidebook: When to use the Study Levels 1 & 2 analyses
Initial Cost
Service Cost
Preventive Maintenance Cost
Operating Cost
Disposal Cost
Select an adaptation strategy to address the risk identified
Account for full life cycle costs of implementing the adaptation strategy
Some factors to consider when deciding if a CBA should be conducted:
  Cost – inexpensive projects might not warrant a CBA; expensive, complex projects might need a detailed CBA
  Project useful life – CBA appropriate for longer-lived projects
  Risk – Projects with high risks could benefit
Determine if only financial benefits from adaptation will be considered, or also environmental and social
  Environmental and social benefits can be difficult to monetize
  If environmental and social benefits are considered, determine if they should be quantitative or qualitative

## Slide 20: Further Research
Extreme heat – Little information currently is publicly available regarding impacts and costs on infrastructure; most studies focus on human health
CBA Tool Development – Could help eliminate a perceived obstacle to using the frameworks by decreasing the amount of data needed to perform analyses
National or multi-state analysis for transportation sector impacts – Parallel and similar to the Zillow analysis completed for flood impacts to the residential sector

## Slide 21: Conclusion
Increasingly frequent weather events can have potentially serious, costly impacts on transportation infrastructure
Transportation practitioners increasingly are trying to incorporate climate adaptation into planning
Climate (and hence design) uncertainty and data requirements are perceived barriers to completing CBAs for projects
CBA can be completed at different levels of detail, depending on need
CBA is a useful tool that can be used to screen projects and adaptation approaches to identify those for further consideration