## Slide 1: NCHRP 03-133: Traffic Signal Design and Operations Strategies for Non-Motorized Users
Pedestrian Recall and Actuation Research:
Preliminary Findings

## Slide 2: NCHRP 03-133: Traffic Signal Design and Operations Strategies for Non-Motorized Users
Develop toolbox of strategies and treatments to make traffic signals work better for peds/bikes

## Slide 3
Pedestrian Recall and Actuation Research: Preliminary Findings

## Slide 4: Pedestrian Recall vs. Pushbutton Actuation
Research Need
  Decision involves a tradeoff between
    Impact on operations (traffic delay, capacity, progression, cycle length)
  Impact on pedestrians (delay, compliance/safety)
 | Short | Medium | Long
Low | Actuation | ? | Recall
Medium | ? | ? | Recall
High | Recall | Recall | Recall
Pedestrian
volume
Vehicle Green Time Need
Pedestrian Volume | Decision
Low | Actuation
Medium | ?
High | Recall

## Slide 5: Research Questions
When would there be a small traffic impact of putting ped phases on recall?
Is there a ped volume threshold to set ped phases on recall?
How is it different for peds crossing major street or side street?

## Slide 6: Research Methodology: Base Model
Microsimulation on a real arterial in Virginia (Route 1)
Coordinated-actuated arterial with 110 seconds cycle length
Focusing on a single (test) intersection that is non-critical (i.e., has slack capacity)
Modeled both peds crossing main arterial and side street
Recall was tested only for peds crossing main arterial (7 sec of Walk and 20 sec of FDW)
  Crosswalk across side street was set to Rest in Walk

## Slide 7: Research Methodology: Scenario Testing and Variables
Side street vehicle green time required as a fraction of Min Ped Green time required (denoted as “SSG”)
0.5
0.6
0.7
0.85
1.0
1.2
Probability of pedestrian demand in a given cycle (denoted as “PP”)
0.1 (4 peds/hr)
0.3 (12 peds/hr)
0.5 (24 peds/hr)
0.7 (42 peds/hr)
0.9 (80 peds/hr)

## Slide 8: Preliminary Results: Delay Change for Peds Crossing the Main Arterial
Chart: Pedestrian Probability (PP)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
 | -6.6204 | -3.863 | -2.7526 | -1.0928 | -0.36541
With small PP, delay change is nearly equal to Walk time
With high PP, almost no change since ped actuation functions like a recall

## Slide 9: Preliminary Results: Delay Change for Peds Crossing the Side Street
Chart: Pedestrian Probability (PP)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
SSG=0.5 | 4.7568 | 3.8678 | 2.8474 | 1.0024 | 0.34443
SSG=0.6 | 4.5216 | 3.8226 | 2.9558 | 0.95975 | 0.39242
SSG=0.7 | 2.7477 | 2.1381 | 1.9482 | 0.76231 | 0.20969
SSG=0.85 | 1.6247 | 1.5505 | 0.99575 | 0.36342 | 0.14087
SSG=1.0 | 1.2558 | 1.0756 | 0.85537 | 0.14812 | 0.075299
SSG=1.2 | 0.26836 | 0.21989 | 0.16857 | 0.11409 | 0.0046218
With high SSG, regardless of ped volume, impact is small
Peds Crossing Main Arterial | Peds Crossing Side Street
-7 seconds 59 seconds to 52 seconds | +5 seconds 8 seconds to 13 seconds
SSG=0.5, PP=0.1 Scenario

## Slide 10: Preliminary Results: Intersection Vehicle Delay
Chart: Pedestrian Probability (PP)
| 0.1 | 0.3 | 0.5 | 0.7 | 0.9
SSG=0.5 | 2.6367 | 2.1176 | 1.557 | 0.80793 | 0.27955
SSG=0.6 | 2.2663 | 1.8363 | 1.3229 | 0.92972 | 0.39755
SSG=0.7 | 1.2408 | 0.99348 | 0.74438 | 0.48608 | 0.18688
SSG=0.85 | 0.39644 | 0.36871 | 0.27073 | 0.082519 | 0.0049451
SSG=1.0 | 0.56421 | 0.67155 | 0.28849 | 0.14372 | 0.089452
SSG=1.2 | 0.14056 | -0.054337 | -0.19138 | 0.055706 | 0.044808
With low PP and SSG, more pronounced impact but still less than 3 seconds
With high SSG, almost no impact on intersection delay

## Slide 11: Preliminary Results: Side Street Phase Green Time Distribution
Only about 20% of the time, vehicle phase requires less than min ped green
About 80% of the time, vehicle phase requires less than min ped green
Minimum Ped Green

## Slide 12: Key Findings
High pedestrian demand:
  Pedestrian recall is appropriate and has no impact on intersection delay
Long side street vehicular phase green time required:
  Regardless of pedestrian demand, pedestrian recall will reduce pedestrian delay with almost no impact on intersection delay
Low pedestrian volumes:
  Pedestrian recall will reduce ped delay by about the same duration of the Walk interval.

## Slide 13: Questions?