## Slide 1: NCHRP 17-78: Understanding and Communicating Reliability of Crash Prediction Models
UNC Highway Safety Research Center
Kittelson and Associates
Persaud and Lyon
NAVIGATS

## Slide 2: Project Team
UNC Highway Safety Research Center (HSRC)
  Raghavan Srinivasan, Daniel Carter, Bo Lan, and Caroline Mozingo
Persaud & Lyon (P&L)
  Bhagwant Persaud and Craig Lyon
Kittelson and Associates (KAI)
  James Bonneson, Erin Ferguson, and Nick Foster
NAVIGATS
  Geni Bahar

## Slide 3: Background
HSM Part C Predictive Method:
  Base model, which is a safety performance function (SPF)
  Crash modification factors (CMFs) to adjust for conditions different from the base conditions
  Calibration factor to adjust the estimate for local conditions
    Product of these factors produces a crash prediction model (CPM)
    HSM has limited information about reliability of predictions from a CPM

## Slide 4: Objectives
Develop guidance for the quantification of the reliability of CPMs for practitioner use;
Develop guidance for user interpretation of model reliability; and
Develop guidance for the application of CPMs accounting for, but not limited to, assumptions, data ranges, and intended and unintended uses.

## Slide 5: Reliability of CPMs
Bias
  Difference between the CPM estimate and the true value
Variance
  Extent of uncertainty in the CPF estimate
Repeatability
  The extent to which multiple analysts using the same CPM with the same training, data sources, and site of interest obtain the same results

## Slide 6: Factors Influencing Reliability
Categories: Model Related & Application Related Factors
Model Related Factors
  Application of CPMs with and without calibration
  Add EB method
  Add CMFs from other sources (consistent with base conditions)
  Updating CPMs for changes over time
  Use jurisdiction-specific base condition SPFs
  Use crash modification functions (CMFunctions) instead of CMFs

## Slide 7: Factors Influencing Reliability: contd.
Application Related Factors
  Error and uncertainty in the input values
  Use of CMFs that are inconsistent with the base conditions of the CPM
  Relative impact of a CPM variable
  Omitted variables in CPM
  Missing application data
  Applications of the CPMs for rare crash types
  Application exceeds the range of an input variable
  Application site has characteristics that are not represented by CPM

## Slide 8: Survey of Practitioners to Assess Importance of Different Factors
Survey was sent to:
  AASHTO Safety Management subcommittee
  AASHTO HSM2 Steering Committee
  FHWA HSM Pooled Fund Group
Respondents were provided with 7 issues and asked to indicate:
  Very concerning
  Somewhat concerning
  Neutral
  Not very concerning
  Not a concern

## Slide 9: Survey of Practitioners, 7 issues
Using CPMs that were developed in another jurisdiction but calibrated for your local jurisdiction
Using CMFs not included in the original CPM but are consistent with the base conditions of the CPMs
Using CMFs not included in the original CPM but are inconsistent with the base conditions of the CPMs
Using a CPM that does not represent the characteristics of your project
Using input values that are uncertain
Using a CPM for a project whose characteristics lie outside the range of the values of the CPM development
Using a CPM to estimate rare crash types

## Slide 10: Focus of the Research Project
Procedures for Quantifying the Reliability of Crash Prediction Model Estimates with a Focus on:
  Mismatch between CMFs and SPF Base Conditions
  Error in Estimated Input Values
  How the Number of Variables in CPM Affects Reliability

## Slide 11: Focus of the Research Project, contd.
Reliability Associated with
  Using a CPM to Estimate Frequency of Rare Crash Types and Severities
  Predicting Outside the Range of Independent Variables
  Predictions Using CPMs Estimated for Other Facility Types

## Slide 12: Objective of This Presentation
Provide an overview of each topic/scenario along with the steps involved in the guidance
Examples and case studies are provided in the following document:
  NCHRP Research Report 983: Reliability of Crash Prediction Models: A Guide for Quantifying and Improving the Reliability of Model Results

## Slide 13: Scenario 1: Reliability of CPM Estimates - Mismatch between CMFs and SPF Base Conditions
CMFs and SPF Base Conditions not Matched
Application Cases
  A. CMFs in predictive model match to base condition variables in SPF
  B. One or more CMFs used with the model do not match with the base condition variables in SPF
  C. One or more CMFs not used, yet the associated base condition exists in the SPF

## Slide 14: Reliability of CPM Estimates - Mismatch between CMFs and SPF Base Conditions
Objectives
  Develop technique to quantify the influence of Cases B and C on reliability of the prediction
  Demonstrate its use to interpret model reliability

## Slide 15: Base Condition Mismatch (Procedures)
Case A: CMF from Part D used with SPF (CMF is consistent with SPF base conditions)
  Step 1. Assemble the data needed to apply the procedure
  Step 2. Compute estimation coefficient
  Step 3. Compute bias adjustment factor
  Step 4. Compute the predicted crash frequency for site of interest

## Slide 16: Base Condition Mismatch (Procedures),Case A, contd.
Case A: CMF from Part D used with SPF (CMF is consistent with SPF base conditions)
  Step 5. Compute the unbiased predicted crash frequency for site of interest
  Step 6. Compute the increased root mean square and coefficient of variation
  Step 7. Compute the amount of bias

## Slide 17: Base Condition Mismatch (Procedures)
Case B: CMFs Do Not Have a Corresponding Base Condition in the SPF
  Step 1. Assemble the data needed to apply the procedure
  Step 2. Compute estimation coefficient
  Step 3. Compute bias adjustment factor
  Step 4. Compute the predicted crash frequency for site of interest

## Slide 18: Base Condition Mismatch (Procedures), Case B, contd.
Case B: CMFs Do Not Have a Corresponding Base Condition in the SPF
  Step 5. Compute the unbiased predicted crash frequency for site of interest
  Step 6. Compute the unbiased overdispersion parameter for the CPM with the external CMF
  Step 7. Compute the increased root mean square and coefficient of variation
  Step 8. Compute the amount of bias

## Slide 19: Base Condition Mismatch (Procedures)
Case C: CMF Not Used in CPM but Base Condition Accommodated in the SPF
  Step 1. Assemble the data needed to apply the procedure
  Step 2. Compute estimation coefficient
  Step 3. Compute bias adjustment factor
  Step 4. Compute the predicted crash frequency for site of interest

## Slide 20: Base Condition Mismatch (Procedures), Case C, contd.
Case C: CMF Not Used in CPM but Base Condition Accommodated in the SPF
  Step 5. Compute the unbiased predicted crash frequency for site of interest
  Step 6. Compute the unbiased overdispersion parameter for the CPM with the omitted CMF
  Step 7. Compute the increased root mean square and coefficient of variation
  Step 8. Compute the amount of bias

## Slide 21: Scenario 2: Error in Estimated Input Values
Significance of uncertain or erroneous input values depends on context of use:
  More significant for estimating effect of a contemplated countermeasure or design change
  Network screening applications may be less impacted
Impact of uncertain or erroneous input values on reliability largely dependent on:
  Degree to which the value is uncertain or erroneous
  How impactful the variable under question is to the CPM prediction

## Slide 22: Error in Estimated Input Values (contd.)
Methods to Assess Potential Reliability
  Guidance developed is a heuristic procedure that practitioners can use to assess how uncertainty or error in their data may affect reliability
  Following types of analysis
    Applying a CPM to predict crash frequency
    Applying a CPM along with crash data for network screening

## Slide 23: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis of Predicted Crash Values
  Step 1. Assemble data
  Step 2. Calibrate the CPM
  Step 3. For each variable in the CPM where measurement error is of concern, assign a random number reflecting the degree to which measurement error is suspected for that variable

## Slide 24: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis of Predicted Crash Values (contd.)
  Step 4. For each variable in the CPM where measurement error is of concern, multiply the recorded value by the random number generated for that variable in Step 3
  Step 5. Apply the CPM twice, once using the original estimated variable values and a second time using the new variable values generated in Step 4

## Slide 25: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis of Predicted Crash Values (contd.)
  Step 6a. Use the values in Step 5 and estimate a series of GOF statistics
  Step 7a. Divide the root mean square difference and the extreme value estimates from Step 6a by the average value of the crash predictions with known values and multiply by 100
  Step 8a. Using the GOF statistics calculated in Step 7a assess the impact of measurement errors on the CPM

## Slide 26: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis for Network Screening
  Steps 1 through 5 are the same as for the previous situation (i.e., Sensitivity Analysis of Predicted Crash Values)
  Step 6b. For each CPM applied, compute either the EB or EB Excess estimate for each site by combining the CPM predicted crash estimate with the observed crash data

## Slide 27: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis for Network Screening (contd.)
  Step 7b. For each CPM applied, rank all locations separately by the network screening measure used (EB Expected or EB Excess)
  Step 8b. For each ranked list determine the Spearman’s correlation coefficient, comparing the rankings using the CPMs with measurement error to the ranking using the CPM with the original estimated values

## Slide 28: Error in Estimated Input Values (Procedural Steps)
Sensitivity Analysis for Network Screening, contd.
  Step 9b: For each ranked list, for the top 30, 50, and 100 sites ranked using the base CPM, the percentage of sites not included in the ranked lists using the CPMs with measurement error is tabulated
  Step 10b: Using the goodness-of-fit measures calculated in Steps 8b and 9b assess the impact of measurement errors on the CPM

## Slide 29: Scenario 3: Effect of Number of Variables in CPM on Reliability
Relative Impact of the Variable, e.g.,
  Left turn volumes are influential predictors of left turn crashes
  Shoulder width may have little influence on total crashes for rural multilane roads
Omitted Variables in the CPM, e.g.,
  Estimating crashes on segments with curves with CPM developed without variable for curvature
Missing Application Data, e.g.,
  Applying CPM in preliminary design before design elements are finalized

## Slide 30: Effect of Number of Variables in CPM on Reliability
Methods to Assess Potential Reliability
  The guidance developed is a heuristic procedure that practitioners can use to assess how the use or absence of additional variables in a CPM affects reliability
  Answer two questions:
    Which of multiple CPMs to apply, particularly when the number of variables varies between SPFs?
    What are the impacts on reliability of using a CPM when not all the variables in the CPM are known?

## Slide 31: Effect of Number of Variables in CPM on Reliability
Procedural Steps
  Step 1. Assemble all data required for applying the CPM
  Step 2. Decide how many alternate CPMs are to be compared and which variables will be included in each
  Step 3. For each CPM being considered, estimate the Modified R2, MAD, dispersion parameter, and the percent of observations outside of two standard deviation limits for the CURE plot for the fitted values
    For each of these measures, divide the values by the value for the full CPM with all variables

## Slide 32: Effect of Number of Variables in CPM on Reliability
Procedural Steps (contd.)
  Step 4. The analyst should decide how many years of observed crash data will be used in their Network Screening program and whether sites are to be screened by the EB Expected or the EB Excess methods
  Step 5. For each ranked list determine the Spearman’s correlation coefficient, comparing the rankings using the CPM with all variables used to the other CPMs in turn.

## Slide 33: Effect of Number of Variables in CPM on Reliability
Procedural Steps (contd.)
  Step 6. For each ranked list, for the top 30, 50, and 100 sites ranked using the full CPM with all variables, the percentage of sites not included in the ranked lists using the alternate CPMs is tabulated.
  Step 7. Using the goodness-of-fit measures calculated in Steps 3, 5, and 6, evaluate the alternate CPMs.

## Slide 34: Scenario 4: Reliability Associated with Using CPM for Rare Crash Types and Severities
Three cases
  Case A: Models did not converge or were illogical (e.g., AADT exponents were negative or statistically insignificant at the 10% level).
  Case B. There is low confidence in a CPM because it did not validate well or had poor GOF statistics.
  Case C: For numerous crash types and severities, estimation of CPMs was not considered either:
    because they are not of primary interest generally (e.g., night crashes), or
    because there are typically too few crashes to attempt SPF development (e.g., bicycle, pedestrian, and fatal crashes).

## Slide 35: Reliability Associated with Using CPM for Rare Crash Types and Severities
For such cases, a two-stage “fixed proportions” approach is applied:
  A crash type/severity proportion developed from the jurisdiction’s data is applied to “parent” CPM prediction, e.g.,
    a KABC parent CPM, if reliable, would be considered for both KA and KAB crashes, and so on.

## Slide 36: Reliability Associated with Using CPM for Rare Crash Types and Severities
If Case A or Case C pertains:
  a crash type/severity proportion developed from the jurisdiction’s data is applied to a prediction from the recommended and calibrated “parent” SPF (assess using GOF statistics)

## Slide 37: Reliability Associated with Using CPM for Rare Crash Types and Severities
If Case B pertains:
  Approach 1: A Case B uncalibrated SPF that did not validate well or has poor GOF statistics.
    Such an SPF may not be presented in the HSM but may be retrieved from another source if and when available
  Approach 2: A modified SPF in which a crash type/severity proportion developed from the jurisdiction’s data is applied to a prediction from the HSM recommended and uncalibrated “parent” SPF

## Slide 38: Reliability Associated with Using CPM for Rare Crash Types and Severities
Illustration Where Case A or C pertains
SPF predictions for same direction (SD), killed and seriously injured (KA) crashes on 4-lane divided (4D) segments
NCHRP Project 17-62 could not estimate base for these crashes because there were none in the database (California)
  Database for another jurisdiction (Illinois) used for model validation contained 8 such crashes.
Question: what SPFs can be used for estimating KA-SD crashes for base conditions in Illinois?

## Slide 39: Reliability Associated with Using CPM for Rare Crash Types and Severities
Illustration Where Case B Pertains
Several base condition SPFs developed in NCHRP Project 17-62 did not validate well or had poor GOF statistics. The illustration here is for one of those:
  Same direction (SD), KAB crashes at 4 leg stop controlled (4ST) intersections on multilane roads. Data used in NCHRP Project 17-62 was based on 12 crashes in Minnesota
NCHRP Project 17-62 validation data for Ohio are used. Dataset contained 12 KAB-SD crashes

## Slide 40: Scenario 5: Predicting Outside the Range of the Independent Variable
HSM states that the application of CPMs to “sites with AADTs substantially outside this range may not provide reliable results”
Data used for estimation versus data used for application
  Range of variables (especially, AADT) may be different
  Distribution of variables may be different even if the range is similar

## Slide 41: Predicting Outside the Range of the Independent Variable
Maximum AADT values for selected CPMs
Note: * Proposed for 2nd edition of the HSM
Roadway Type | Source of CPM | Maximum AADT (veh/day)
Rural Two-Lane Road Segments | SafetyAnalyst | 30,025
 | 1st edition of the HSM | 17,800
 | NCHRP Project 17-62* | 21,622
Rural Multilane Undivided Segments | SafetyAnalyst | 42,638
 | 1st edition of the HSM | 33,200
 | NCHRP Project 17-62* | 21,667
Rural Multilane Divided Segments | SafetyAnalyst | 31,188
 | 1st edition of the HSM | 89,300
 | NCHRP Project 17-62* | 66,504

## Slide 42: Predicting Outside the Range of the Independent Variable
Implicit Assumption – functional form of SPFs is applicable/valid outside the range of estimation data – bias in prediction may depend on relationship between crashes and site characteristics

## Slide 43: Predicting Outside the Range of the Independent Variable
Objective – Reliability of using the CPMs to predict the number of crashes at sites whose site characteristics (especially, AADT) are outside the range of the data used to estimate the CPMs

## Slide 44: Predicting Outside the Range of the Independent Variable
Different options
  Option 1: Perform calibration
  Option 2: Adjust parameter/coefficient for AADT and perform calibration
  Option 3: Estimate calibration function or SPF by modifying the coefficient for AADT and perform calibration
  Option 4: Estimate calibration function or SPF and perform calibration
  Option 5: Estimate calibration function or SPF with different parameters for AADT and the other factors, and perform calibration

## Slide 45: Predicting Outside the Range of the Independent Variable
Illustration of the 5 options using HSIS data (2005 to 2014) from California freeways
  Exclude ramp influence areas for this illustration
  Exclude segments shorter than 0.01 miles
  Categorize data by number of lanes, terrain, area type (rural or urban)
  For the different freeway categories, SPFs were estimated using data from segments with lower AADT values, and they were tested using data from segments with higher AADT values

## Slide 46: Scenario 6: Reliability Associated with Predictions Using CPMs Estimated for Other Facility Types
2nd edition of the HSM will provide CPMs for many facility types
  There may be facility types for which specific CPMs will not be available
Reliability may depend on
  Functional form of CPM
  Range of site characteristics

## Slide 47: Reliability Associated with Predictions Using CPMs Estimated for Other Facility Types

## Slide 48: Reliability Associated with Predictions Using CPMs Estimated for Other Facility Types
Objective – Provide guidance on the reliability of using the CPMs to predict the number of crashes at a different facility type
Illustration of the Problem using HSIS data from California:
  Estimation Group (facility types used for estimating CPMs)
  Application Group (facility types used for applying the CPMs)

## Slide 49: Reliability Associated with Predictions Using CPMs Estimated for Other Facility Types
Group | Facility Types used for Estimating CPMs (estimation group) |  | Facility Types Used for Applying the Estimated CPMs (application group) |  | Crash Types
 | Facility type | Segments | Facility type | Segments | 
Group 1 | Rural 4 lane, Flat terrain | 1075 | Rural 6 lane, Flat terrain | 102 | SV, MV, Total
 | Urban 6 lane, Flat terrain | 437 |  |  | 
Group 2 | Rural 4 lane, Flat terrain | 1075 | Urban 4 lane, Flat terrain | 428 | SV, MV, Total
 | Urban 6 lane, Flat terrain | 437 |  |  | 
Group 3 | Rural 4 lane, Rolling terrain | 421 | Rural 6 lane, Rolling terrain | 58 | SV, MV, Total
 | Urban 6 lane, Rolling terrain | 253 |  |  | 
Group 4 | Rural 4 lane, Rolling terrain | 421 | Urban 4lane, Rolling terrain | 263 | SV, MV, Total
 | Urban 6 lane, Rolling terrain | 253 |  |  | 

## Slide 50: NCHRP Project 17-78 Products
NCHRP Web-Only Document 303
NCHRP Research Report 983: Reliability of Crash Prediction Models: A Guide for Quantifying and Improving the Reliability of Model Results
Communications Plan
One-page flyer