## Slide 1: NCHRP 03-137: Algorithms to Convert Basic Safety Messages into Traffic Measures Final Project Presentation
National Cooperative Highway Research Program Transportation Research Board of The National Academies

## Slide 2: NCHRP is sponsored by the individual state departments of transportation of the American Association of State Highway and Transportation Officials. NCHRP is administered by the Transportation Research Board (TRB), part of the National Academies of Sciences, Engineering, and Medicine, under a cooperative agreement with the Federal Highway Administration (FHWA). Any opinions and conclusions expressed or implied in resulting research products are those of the individuals and organizations who performed the research and are not necessarily those of TRB; the National Academies of Sciences, Engineering, and Medicine; the FHWA; or NCHRP sponsors.

## Slide 3: NCHRP Research Outcome
Position state and local agencies to take early advantage of Basic Safety Messages (BSM) to:
  reduce cost,
  improve accuracy, and
  add new measures to their systems management capabilities.
Examples of high-value use cases:
  Early detection of queues from broadcast BSM can help traffic managers take proactive decisions (e.g., dispatch maintenance crew to fix a broken water hydrant)
  Presence/location of incidents can be detected rapidly to allow traffic managers to take actions (e.g., dispatch first responders, dispatch maintenance crew, re-route traffic)
  BSM can be used to provide reliable traveler information (e.g., travel times) even on facilities without traditional sensors
Notes: 3

## Slide 4: Project Team
Meenakshy Vasudevan, Ph.D., PMP
Principal Investigator
Noblis
Karl Wunderlich, Ph.D., PMP
Director of Surface Transportation
Noblis
James O’Hara, CSM
Software Developer
Noblis
Haley Townsend, SSM
Data Scientist
Noblis
Sampson Asare, Ph.D., PMP
Sr. Transportation Engineer
Noblis
Syihan Muhammed, CSM
Programmer
Noblis
Kaan Ozbay, Ph.D.
Professor and Director of C2SMART
New York University (NYU)
Di Yang
Research Assistant and Ph.D. Candidate
NYU
Jingqin (Jannie) Gao, Ph.D.
Sr. Researcher
NYU
Abdullah Kurkcu, Ph.D.
Lead Traffic Modeler
Ulteig (formerly NYU)
Fan Zuo
Research Assistant and Ph.D. Candidate
NYU

## Slide 5
Mo Zhao, Ph.D., Panel Chair
Research Scientist
Virginia Department of Transportation (VDOT)
Matthew W. Bond
District Traffic Engineer
Virginia DOT (VDOT)
Marco D. Cameron, P.E.
Traffic Operations Division
Texas DOT (TxDOT)
Nikola Ivanov, PMP
Director of Operations/COO
Center for Advanced Transportation Technology Laboratory (CATT Lab)
Taylor Li, Ph.D., P.E.
Assistant Professor
University of Texas at Arlington
Andrew J. Robinson
Director of Technology
Event Dynamic
Ray A. Starr
Assistant State Traffic Engineer
Minnesota DOT (MnDOT)
Jason (Xianding) Tao, Ph.D.
Senior ITS Engineer
Washington, DC DOT (DDOT)
Jon Obenberger, Ph.D., P.E., FHWA Liaison
Transportation Operations Engineer
FHWA Office of Operations Research and Development
Project Panel

## Slide 6: Project Overview
Project Objectives
Develop and validate algorithms that will use BSM data to estimate selected traffic measures (performance monitoring, traffic control, traveler information)
Period of Performance
1 August 2019 – 30 November 2021 (28 months)
Task 0: Project Mgmt
Task 1:
Literature Review
Task 2:
Measures Identification
Task 3:
Interim Report
Task 4:
Algorithm Development
Task 5:
Algorithm Validation
Task 6:
Algorithm Publishing
Task 7:
Final Deliverables
Phase I
Phase II
Go/No-Go
(4/20/20)
Task 3: In-Person Meeting (1/8/20)
Task 4: Virtual Meeting (11/17/20)
Task 5: Virtual Meeting (4/8/21)
Task 2: In-Person Meeting (10/17/19)
Notes: 6

## Slide 7: Literature Review to Identify Existing Algorithms
PURPOSE
Conduct literature review to identify existing algorithms that convert BSM to traffic measures to avoid duplication of efforts and identify gaps in traffic measures research
KEY FINDINGS FROM LITERATURE REVIEW & STAKEHOLDER INPUT (#1 of 2)
Most of the reviewed algorithms that convert BSM into traffic measures:
  are focused on safety measures, with limited research on mobility measures, especially for non-recurrent congestion or adverse weather conditions
  do not factor vehicle ID privacy into their logic
  assume perfect and reliable communication between connected vehicles (CV) and back-end infrastructure
  are unable to estimate accurate lane-specific measures
  show limited use of certain BSM elements for measures estimation
  have low accuracy under low CV market penetration rates
  have undergone limited rigorous testing or field validation
  will require increased computational processing needs with increase in CV market penetration
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 8: Literature Review to Identify Existing Algorithms
KEY FINDINGS FROM LITERATURE REVIEW & STAKEHOLDER INPUT (#2 of 2)
There is a need to develop algorithms for real-world operations.
There is a need for open-source algorithms to estimate measures, for potential adaptation by agencies and practitioners.
There is limited capability to accurately estimate localized measures, such as traffic density, volume, and occupancy from BSM.
Fusing BSM data with data from other sources as well as synchronization of timescales are key challenges in BSM-based measures estimation, but there is limited literature on how this is addressed.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 9: Identify, Prioritize, & Down-Select Traffic Measures
PURPOSE
Identify key traffic measures that are commonly used by agencies for performance monitoring, traffic control, and traveler information
Describe how BSM data will be used to estimate commonly used traffic measures
Down-select specific measures that will be considered for scalable algorithm development, with input from NCHRP Panel
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 10: Candidate Mobility Measures
Measure | Definition
Queue length | A vehicle is in queue when it is either stopped or traveling at a speed less than 10 ft/s (3 m/s) and is approaching another queued vehicle at headway of less than 20 ft (6 m)
Shockwaves | Transition zones between two traffic states (e.g., from free flow to at capacity to congested)
Arrival Volumes | Number of vehicles arriving at a point on a roadway, or a given lane or direction of highway, during a specified time interval
Density | Number of vehicles occupying a given length of the highway in a traffic lane
Stops | Defined as a vehicle which has come to a complete stop or a vehicle traveling below a specified speed threshold
Delay | Travel time in excess of the free flow travel time for a specific time interval
Speed | Average speed of vehicles traversing pre-specified segments in a specific time interval
Travel Time | Average time necessary to traverse a route between any two points of interest for trips that start within a specific time interval
Mean Time to Detect and Verify Incidents | Average time to detect and verify the presence of incidents on a roadway
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 11: Candidate Safety Measures Using Individual Vehicle Trajectories
Measure | Definition
Fast Acceleration | Vehicle longitudinal acceleration larger than a certain threshold.
Hard Braking | Vehicle longitudinal deceleration greater than a certain threshold.
Extreme Lane Change | Vehicle lateral acceleration less than or greater than certain thresholds.
Minimum Vehicle Jerk | Vehicle jerk less than a certain threshold.
Maximum Vehicle Jerk | Vehicle jerk greater than a certain threshold.
Peak-to-Peak Jerk | The peak-to-peak jerk is defined as the difference between the maximum positive jerk and minimum negative jerk during one braking event that exceeds a certain threshold.
Instantaneous Driving Volatility | For each speed bin (e.g., 0.5 mph), an instantaneous driving volatility is identified if more than five successive BSMs (> 0.5 seconds) are beyond the 95th percentile (the proposed threshold) of the directional acceleration (vector sum of longitudinal acceleration and deceleration) in that speed bin.
Time to Collision | The time required for two vehicles to collide if they continue at their present speeds and on the same path.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 12: Candidate Safety Measures Using Multiple Vehicle Trajectories
Measure | Definition
Modified Time To Collision | Time to collision modified by including acceleration/deceleration of the following vehicle.
Time To Collision with Disturbance | Time to collision modified by imposing a hypothetical acceleration/deceleration to the leading vehicle.
Deceleration Rate to Avoid Collision | The minimum deceleration rate required by the following vehicle to come to a timely stop (or match the leading vehicle’s speed) and hence to avoid a crash.
Post-Encroachment Time | The time from the end of right-of-way infringement of the first vehicle to the second vehicle reaching the conflict spots, measured from the rear bumper of the first vehicle to the front bumper of the second vehicle.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 13: Identify, Prioritize, & Down-Select Traffic Measures
Criteria for down-selecting mobility and safety traffic measures:
Criterion | Definition
Utility | Identifies the value of the measure for the following needs: (i) performance monitoring, (ii) traffic control, (iii) roadway weather information, (iv) work zone information, or (v) traveler information
Complexity | Identifies the technical complexity for developing an algorithm for estimating the measure using BSM
Accuracy at Low Market Penetrations | Identifies the possibility of the measure being estimated accurately even at low market penetration of connected vehicles (i.e., in near term)
Real-Time Operations Criticality | Identifies the criticality of the measure to support real-time operations
Resources | Identifies the possibility of measure being developed with the available project funds
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 14: Down-Selected High Priority Mobility and Safety Measures
Type | Down-Selected Measures
Mobility | Travel Time Space Mean Speed Queue Length Mean Time to Detect and Verify Incidents
Safety | Hard Braking Deceleration Rate to Avoid Collision (DRAC) Time-To-Collision with Disturbance (TTCD)
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 15: Algorithm Development
PURPOSE
Develop and test the seven high-priority mobility and safety measure estimation algorithms
  Using emulated BSMs generated from simulated vehicle trajectories with U.S. DOT’s open source Trajectory Conversion Algorithm (TCA) tool (https://github.com/OSADP/TCA)
Algorithm Development and Test Data Specifications | 
Market Penetration Rate of CVs | 5%, 20%, 50%, 75%
Communication Network Protocol | Dedicated Short-Range Communications (DSRC) with no gaps or errors in communication
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 16: Algorithm Development Data for Mobility Measures
Measure | Simulated Network | Simulation Software | Software Source
Travel Time, Space Mean Speed, Mean Time to Detect and Verify Incidents | I-405, Seattle, WA 29.5-mile corridor Freeway with significant travel time variability subject to periods of high travel demand and resultant congestion | VISSIM model calibrated to representative days for six operational conditions (e.g., low demand, weather and incidents, etc.) | Washington State DOT and USDOT (2019)
Queue Length | 12th and 14th Street, Jersey City, NJ 1.4 miles x 2 miles with 65 signalized intersections (only 4 signalized intersections were used for development) Dense urban grid with severe congestion | PARAMICS model calibrated to AM peak average | New York University UrbanMITS Laboratory and Rutgers RIME Laboratory (2016)
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 17: Algorithm Development Data for Safety Measures
Measure | Simulated Network | Simulation Software | Software Source
Hard Braking Deceleration Rate to Avoid Collision (DRAC) Time-To-Collision with Disturbance (TTCD) | New Jersey Turnpike (NJTPK) / Jersey City, NJ NJTPK Newark Bay-Hudson County Extension (NB-HCE): Exit 14 to Holland Tunnel, 7 miles x 3 miles Urban freeway with moderate congestion (NJTPK); Dense urban grid with severe congestion (Jersey City) | PARAMICS model calibrated to AM peak average | New York University UrbanMITS Laboratory and Rutgers RIME Laboratory (2016)
Hard Braking, DRAC, TTCD | Flatbush Ave, New York City, NY 1.6 miles x 0.7 miles with 17 intersections Urban arterial corridor with severe congestion | Simulation of Urban Mobility (SUMO) model calibrated to AM peak average | New York City Department of Transportation (2020)
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 18: Algorithm Development Approach using Nearest Neighbor Technique
Travel Time
  Use nearest neighbor search to build a trip for a hypothetical vehicle
  Search for BSMs within a pre-defined time-distance window
  Calculate travel time experienced by the hypothetical vehicle along a route
  This represents the average travel time of vehicles along the route at that time
Space Mean Speed
  Use Travel Time algorithm for shorter roadway segments (~ 1 mile)
  Calculate as length of the segment divided by the hypothetical vehicle travel time over the segment
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 19: Algorithm Development Approach using Machine Learning
Mean Time to Detect and Verify Incidents
  Develop a supervised machine learning (ML) algorithm (i.e., Neural Network)
  Use simulated incidents as ground truth and features engineered from TCA-generated BSMs
  Rapidly detect a potential incident and verify it within roadway links every 5 seconds
Queue Length
  Develop a supervised ML algorithm (i.e., Random Forest)
  Use the calculated ground truth queues and features engineered from TCA-generated BSMs
  Rapidly classify maximum queue counts (and derive queue lengths) per roadway link every 30 seconds
Data Creation
Link Assignment
Data Processing
Feature Engineering
ML Preparation
ML Train & Test
Machine Learning Development Process
Data Preparation Stages
Machine Learning Stages
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 20: Algorithm Development Approach for Safety Measures (#1 of 2)
Hard Braking
  Use a pre-determined threshold for each timestamped vehicle’s deceleration rate to identify hard braking events
  Develop algorithms (both off-line and on-line modes) to determine the optimal thresholds and the minimum required market penetration rate (MPR)
Deceleration Rate to Avoid Collision (DRAC)
  Pair vehicles and use a pre-determined threshold and relative angle (<30 degree) to identify events
    Vehicle IDs are paired at each timestamp if they are close to each other (~ 50 feet)
  Develop algorithms (both off-line and on-line modes) to determine the optimal thresholds and the minimum required MPR
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 21: Algorithm Development Approach for Safety Measures (#2 of 2)
Time-To-Collision with Disturbance (TTCD)
  Calculate the risk by sampling from the pre-defined disturbance distribution
    Hypothetical disturbance is calibrated using field data and tested for sensitivity
  Impose the sampled disturbance values to identify vehicle pairs
    Vehicle IDs are paired at each timestamp if they are close to each other (~ 50 feet)
  Develop algorithms (off-line mode) to determine the optimal thresholds, the minimum required MPR, and the minimum number of Monte Carlo (MC) simulation runs
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 22: Algorithm Validation (#1 of 2)
Measure | Simulated Network | Simulation Software | Software Source
Travel Time, Space Mean Speed | I-78, Jersey City, NJ (simulated) 2.1-mile corridor Major commuter freeway corridor in dense urban grid with severe congestion and toll plaza | PARAMICS model calibrated to AM peak average | New York University UrbanMITS Laboratory and Rutgers RIME Laboratory (2016)
Mean Time to Detect and Verify Incidents, Queue Length | Flatbush Ave, New York City, NY (simulated) 1.6 miles x 0.7 miles with 17 intersections (only 6 signalized intersections were used for queue length validation) Urban arterial corridor with severe congestion | SUMO model calibrated to AM peak average | New York City Department of Transportation (2020)
PURPOSE
Validate the seven high-priority mobility and safety algorithms using simulated and/or field data
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 23: Algorithm Validation (#2 of 2)
Measure | Network | Field Data Source
Hard Braking, DRAC, TTCD | Flatbush Ave & Tillary St intersection, Brooklyn, NY (field) A major four-leg signalized intersection along the Flatbush Ave urban arterial corridor | Drone-recorded traffic surveillance videos
Hard Braking, DRAC, TTCD | Franklin D. Roosevelt (FDR) freeway, Manhattan, NY (field) An approximately 260-feet urban freeway segment with mild congestion | Street-level traffic camera-recorded videos
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 24: Algorithm Validation Results for Mobility Measures
Mobility Measure | Metric | 5 MPR | 20 MPR | 50 MPR | 75 MPR
Travel Time | Mean Absolute Percentage Error (MAPE) | 9.9% | 10.8% | 11.6% | 11.7%
Space Mean Speed | MAPE | 12.9% | 13.8% | 15.1% | 15.7%
Queue Length | Accuracy | 66.3% | 71.3% | 75.1% | 78.8%
Mean Time to Detect Incidents | True Positive Rate (TPR) / False Positive Rate (FPR) | -- | 15.6% / 0.09% | -- | 32.0% / 0.08%
Mean Time to Verify Incidents | TPR / FPR | -- | 100% / 0.005% | -- | 100% / 0.016%
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 25: Algorithm Validation Results for Safety Measures
Validation Results for the three safety measures (hard braking, DRAC, TTCD)
  Correlation with Crashes: Positive correlations were found between safety risk events and crashes. Correlation coefficients between the three safety measures and crashes are found to be positive for optimal threshold values and window size(s).
  MPR Determination Method 1 – Correlation Method: Shapes of the curves obtained from field data were similar to those obtained from simulated data in most cases.
  MPR Determination Method 2 – Elbow Method: Shapes of the curves obtained from field data were similar to those obtained from simulated data in most cases.
  Note: Real-world trajectory data were used for algorithm validation.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 26: Key Takeaways for Mobility Measures Using Machine Learning
Machine learning (ML) models were developed for Queue Length and Mean Time to Detect and Verify Incidents.
  With the ML approach, the queue length application demonstrated significant improvements in terms of accuracy over previous heuristics for queue length estimation.
  The ML algorithms scale well to meet big data challenges.
Training localized models (e.g., to the specific network) is necessary to achieve adequate performance when relying solely on sparse BSM data.
  Models perform best when trained and tuned to the specific flow and characteristics of the network.
The ML models can be exported, re-trained, and applied by agencies.
The project resulted in a variety of BSM-based features engineered for queue classification and mean time to detect and verify incidents that can be re-used for training ML models for other measures.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 27: Key Takeaways for Mobility Measures Using Nearest Neighbor Search
Nearest neighbor search methods were used for both Travel time and Space Mean Speeds estimations.
The applications resulted in similar accuracy as previous work by the authors but are now set up to operate in real time.
Key takeaways are summarized below:
  Need to localize parameters. Performance improves when algorithm parameters such as search window time and distance are calibrated to the location.
  Accuracy is highly dependent on mapping input. Algorithm accuracy can be greatly improved by highly accurate mapping of roadways and creation of hypothetical vehicle paths that account for curvature.
  Run time increases at a higher rate when the number of hypothetical vehicles being tracked increases (due to number of routes or facilities/superlinks being tracked), than when the number of BSMs increases.
  Implementation of algorithms is dependent on management needs and coverage area.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 28: Key Takeaways for Safety Measures
Data smoothing is not necessary for HB and DRAC off-line algorithms but can improve the performance of DRAC on-line and TTCD algorithms if field collected vehicle trajectories are used.
Tests with different results across development/testing and validation could be due to the limited field-collected data (i.e., small sample size).
All three safety measure algorithms can be used for off-line applications.
The hard braking algorithm can be applied for real-time operation while the DRAC algorithm is feasible for near real-time applications, such as adjusting signal timing and speed limit.
DRAC and TTCD algorithms can overcome the lack of off-the-shelf software for calculating these two safety measures.
The algorithms can be used for safety performance evaluation, hotspots identification, safety countermeasure development, and the determination of the minimum deployment size of CVs.
The three safety measure algorithms can be directly applied to both simulated and field-collected BSMs.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 29: Key Contributions
The project team developed, tested, and validated algorithms to convert BSMs into seven high-priority measures of interest to the NCHRP 03-137 Project panel.
These mobility and safety algorithms demonstrated improvements upon existing methods in one or more ways (e.g., accuracy, performance/computation time, use of field data, etc.)
The code and supporting documentation for the seven measures are being made available as open source so the transportation community can tailor them to their specific corridors and facilities for performance monitoring, traffic control, and traveler information.
The algorithms provide agencies a much-needed starting point for leveraging their own connected vehicle data to estimate safety and mobility measures.
These findings and contributions advance data processing and algorithm development in ITS, particularly in the machine learning space.
Lessons learned can help influence the ITS and CV data world, improving the guidance and quality of methods overall.
Having agencies tailor these algorithms to their specific implementations would likely result in additional lessons learned and continue to advance the state of ITS and CV practices.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables

## Slide 30: Recommendations to Practitioners
Review the current context to understand developments made since publication of the project products.
Identify a use case relevant to your agency that could benefit from new or improved safety or mobility measures estimation using BSMs.
Assess the availability of data and other resources to support the use case:
  Assess the algorithm data needs and the availability of data from either CV or other data sources.
  Identify constraints specific to your local corridors/facilities and environment.
  Consider using commercial data and/or services if resources are limited.
Assess the availability and maturity of your IT infrastructure and skillset to support big data processes (specifically for algorithms that use machine learning methods).
Collaborate with agencies for best practices, understanding, and experience using documents and code developed by the project.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables
Notes: 30

## Slide 31: Recommendations for Future Research
Develop algorithms for real-world operations.
Develop techniques to fuse BSM with other data sets and address data synchronization issues.
Develop algorithms for measures such as traffic density, traffic volume, and detector occupancy.
Improve accuracy of lane-specific measures.
Explore the use of less commonly used BSM elements to develop traffic measure estimation algorithms.
Develop algorithms that account for the privacy of CVs.
Develop algorithms that incorporate potential connectivity issues.
Develop algorithms using BSM generated by dynamically altering the capture rates depending on current needs.
Literature Review
Measures Identification
Algorithm Development
Algorithm Validation
Algorithm Publishing
Final Deliverables
Notes: 31